## Slide 1: CPU Hardware
UMBC Graphics for Games

## Slide 2: Models of Behavior
All of CS is built on simplified models of how things work
  Don’t need to know differential equations for transistors to program
  Models allow you to reason about performance
Compare to Physics
  An atom is … The smallest unit of matter? A nucleus with electrons orbiting around it? A nucleus with electron probability clouds? A complex collection of quarks?
Model misses something important?
  Code is not as fast as it could be
  Trying to make it faster might actually make it slower

## Slide 3: Traditional CPU Model
CPUs execute instructions sequentially
Arithmetic operations are a small fixed cost
Memory accesses are free
Branches are free

## Slide 4: Real CPU Architecture
Start 1-4 instructions per cycle
Pipelined, takes 8-16 cycles to complete
  Potentially 50-100 instructions in flight at any one time
Memory is slow
  1 cycle for registers ≈ 20 = 1
  2-4 cycles for L1 cache ≈ 22 = 4
  10-20 cycles for L2 cache ≈ 24 = 16
  50-70 cycles for L3 cache ≈ 26 = 64
  200-300 cycles for memory ≈ 28 = 256

## Slide 5: CPU Goals
Make one thread go very fast
  Avoid pipeline stalls
Branch prediction
  Don’t wait to know branch target (misprediction ~64 instructions)
Out-of-order execution
  Don’t wait for one instruction to finish before starting others
Memory prefetch
  Recognize common access patterns, get data to fast levels of cache early
Big caches
  Though bigger caches add latency

## Slide 6: Revised CPU Model
CPUs execute instructions sequentially
Arithmetic operations are a small fixed cost
Random memory accesses are expensive
Unpredictable branches are expensive

## Slide 7: CPU Performance Tips
Avoid unpredictable branches
  Specialize code
  Avoid virtual functions when possible
  Sort similar cases together
Avoid caching data you don’t use
  Takes time to fetch, takes cache space that could be used for useful data
  Structure of Arrays organization
    struct{P, V}[N] vs. struct{P[N], V[N]}
Avoid unpredictable access
  O(N) linear search faster than O(log N) binary up to 50-100 elements
    Linear access = can prefetch; branch predictable (keep looping) until final iteration
  Asymptotically worse, but for small N, constants matter
  Don’t underestimate how big small N can be

## Slide 8: Entity Component Systems
Compact lists of each type of component
  Physics component, collision component, rendering component
  Fast cache- and branch-friendly iteration over components
Mapping from each entity to its components (& back)
  Reference / pointer in entity?
  Entity ID with hash map?

## Slide 9: Data Oriented Design
General term for optimizing for cache and branch performance
Organize data into compact tables
  E.g. components, though often finer grained
  Functions process or transform tables
  Tables of active elements avoid branching
Data organization ends up looking very similar to database tables

## Slide 10: Data Oriented Design Choices
Prefer arrays over linked lists
  Linked list traversal = likely cache miss at each link
Cross linked hash(key) ➞ index / dense array(index) ➞ (key,data)
  Allow fast processing of elements
  Also SOA form: KeyArray(index) ➞ key; DataArray(index) ➞ data
  If hash uses open addressing, may use index in hash table instead of key
Prefer functions operating on arrays to member functions
  Avoid branching in processing loop
  Avoid virtual functions

## Slide 11: Packed-table Transforms
Generate
  Create list from external source; procedural generation
In-place
  Operate on elements; transform elements
A to B transform
  Generate one list from another; Filter list to active elements
Dispatch
  Generate sub-lists; Split for parallelization
Gather
  Combine multiple lists into one