## Slide 1: Light, Color & Perception
CMSC 435/634

## Slide 2: Light
Electromagnetic wave
  E & M perpendicular to each other & direction
Photon wavelength l, frequency f = c/l
  Visbile l ≈ 380 nm (blue) to 720 nm (red)
Photon energy q = h f = h c/l (in J)
  h = Planck’s constant
Spectral energy Q = J/nm

## Slide 3: Radiometric Units
Term | Symbol | Units
Spectral Energy | Q | J
Spectral Power |  = dQ/dt | W = J/s
Irradiance | E = d/dA | W/m2
Radiance | L = d2/(d dA) | W/(sr m2)
Radiant Intensity | I = d/d | W/sr
/nm dropped by graphics convention

## Slide 4: Light
Infinite-dimensional function vector space
  spectrum(l)
Shine two lights on something adds energies
Scale light energy, scales the intensity

## Slide 5: Color Perception

## Slide 6: Color Perception
Cones = function dot product
Projects to a 3D subspace
metamer = different spectrum, looks the same
Can transform to any 3D linear basis

## Slide 7: Linear Bases
Additive (light)
  Tristimulus (SLM cone response)
  CIE XYZ (from color matching experiments)
  RGB (different for each device)
  Yuv, YCrCb, …
Subtractive (pigment)
  CMY = 1-RGB (grade school Blue, Red, Yellow)
  CMYK

## Slide 8: Photometric Units
Visual intensity
Term | Symbol | Units
Luminous Energy | Q | talbot
Lumens |  = dQ/dt | lm = talbot/s
Illuminance (Lux) | E = d/dA | lx = lm/m2
Luminance | L = d2/(d dA) | lm/(sr m2)
Candelas | I = d/d | cd = lm/sr

## Slide 9: Nonlinear Color Picking
HSV: Cylindrical Coordinates
  Hue = angle
  Saturation = distance from central axis
  Value = distance along axis

## Slide 10: Nonlinear Perception
Linear colors don’t look uniformly different
Nonlinear Luminance
  Gamma (sRGB), L*uv
Nonlinear Luminance & Color
  L*u*v*, L*a*b*
  Can measure color distances
Nonlinear colors do not add

## Slide 11: Adaptation
White point
  Measure as equivalent to black body ºK
  Red-Orange-Yellow-Blue-White
  Incandescent,
Dynamic range (HDR)
  Dark room vs. Sunny day

## Slide 12: Tone Mapping
Convert HDR to LDR
  Global intensity
  Local intensity
  Time
Film exposure
  Aperture, shutter speed, ISO