## Slide 1: Displays
CMSC 435/634

## Slide 2: Light
Visible Range: 390-700nm
Luminance has large dynamic range
  0.00003 Moonless overcast night sky
  30. Sky on overcast day
  30000. Sky on clear day
  16,000. Snowy ground in full sunlight
Actual colors result from spectral curves
  dominant wavelength, hue
  brightness, lightness
  purity, saturation

## Slide 3: Physiology
Rods
  active at low light levels (scotopic vision)
  only one wavelength sensitivity function
Cones
  active at normal light levels
  three types: sensitivity functions with different peaks

## Slide 4: Spectral Sensitivity

## Slide 5: Gamut

## Slide 6: Additive Color Mixing

## Slide 7: Random/Vector Display

## Slide 8: Examples of Random Scan

## Slide 9: Examples of Random Scan

## Slide 10: Examples of Random Scan

## Slide 11: Raster Display

## Slide 12: Raster Display
Each left-to-right trace is called a scan line
Each spot on the screen is called a pixel
Beam turned off to swipe back and up screen
  Called a retrace or blanking interval

## Slide 13: Vector vs. Raster

## Slide 14: Gamma

## Slide 15: Gamma Correction

## Slide 16: Color CRT
Electron guns
Electron beams
Focusing coils
Deflection coils
Anode connection
Shadow mask
Phosphor with RGB zones
Phosphor / Mask close-up

## Slide 17: Color CRT
Uses triads of red, green & blue at each pixel
Uses 3 electron guns – one for each color
Shadow mask used to make each kind of phosphor only visible from one gun

## Slide 18: Liquid Crystal Display (LCD)‏
Light enters polarizer
Nematic crystals twist based on voltage
Allowing light to pass through to other polarizer

## Slide 19: Passive Matrix
Two glass layers
One layer is given vertical transparent conductive material, the other is given horizontal
Integrated circuit sends charge/ground activation to complete circuit at given row/column
Simple, but slow response time

## Slide 20: Active Matrix
Active matrix displays have a transistor at each cell
  Thin film transistor (TFT)
Much faster crystal switching

## Slide 21: Color LCD

## Slide 22: DLP Projector

## Slide 23: DLP Projector

## Slide 24: Laser Printer

## Slide 25: Ink Jet Printer

## Slide 26: Auto-stereo Display: Barrier

## Slide 27: Auto-stereo Display: Lenticular