## Slide 1: Graphics Hardware
CMSC 435/634

## Slide 2: A Graphics Pipeline
Transform
Clip
Rasterize
Shade
Z-buffer
Interpolate
Vertex
Fragment
Triangle

## Slide 3: Computation and Bandwidth
307 GFLOPS
20.5 TFLOPS
7.2 GB/s
14.4 GB/s
2.6 TB/s Texture
106 GB/s Fragment
Vertex
Triangle
Fragment
Based on:
• 100 Mtri/sec (1.6M/frame@60Hz)
• 300 Mvert/sec
• 50 bytes vertex data (pos,norm,tang,uv)
• 50 bytes interpolated
• 68 Bytes fragment output
• 5x depth complexity
• 16 4-Byte textures
• 1024 ops/vert
• 1024 ops/frag
• No caching
• No compression

## Slide 4: Data Parallel
Task
Task
Task
Task
Distribute
Merge

## Slide 5: Sort First
Vertex
Distribute objects by screen tile
Triangle
Fragment
Some pixels
Vertex
Triangle
Fragment
Vertex
Triangle
Fragment
Objects
Screen

## Slide 6: Sort Middle
Vertex
Distribute objects or vertices
Merge & Redistribute by screen location
Vertex
Vertex
Triangle
Fragment
Triangle
Fragment
Triangle
Fragment
Triangle
Fragment
Some pixels
Some objects
Objects
Screen

## Slide 7: Screen Subdivision
Tiled
Interleaved

## Slide 8: Sort Last
Vertex
Triangle
Fragment
Distribute by object
Z-merge
Vertex
Triangle
Fragment
Vertex
Triangle
Fragment
Full Screen
Some objects
Objects
Screen

## Slide 9: Graphics Processing Unit (GPU)
Sort Middle(ish)
Fixed-Function HW for clip/cull, raster, texturing, Ztest
Programmable stages
Commands in, pixels out

## Slide 10: Architecture: Latency
CPU: Make one thread go very fast
Avoid the stalls
  Branch prediction
  Out-of-order execution
  Memory prefetch
  Big caches
GPU: Make 1000 threads go very fast
Hide the stalls
  HW thread scheduler
  Swap threads to hide stalls

## Slide 11: Architecture (MIMD vs SIMD)
MIMD (CPU-Like)
SIMD (GPU-Like)
Flexibility
Horsepower
Ease of Use
(AMD K10 chip-architect.org)
(NVIDIA Volta / wikichip.org)
Actual computational Units

## Slide 12: SIMD Branching
if( x ) // mask threads
{
// issue instructions
}
else // invert mask
{
// issue instructions
} // unmask
Threads agree
or
Threads disagree
THEN

## Slide 13: SIMD Looping
while(x) // update mask
{
// do stuff
}
Everyone runs as long as slowest
Active
Inactive
% Active = Utilization
This example: 36% utilization

## Slide 14: GPU graphics processing model
Z-Buffer
Rasterize
Vertex
Fragment
CPU
Pixels
Texture/Buffer

## Slide 15: NVIDIA GeForce 6
[Kilgaraff and Fernando, GPU Gems 2]
Vertex
Rasterize
Fragment
Z-Buffer
Displayed
Pixels

## Slide 16: GPU graphics processing model
Z-Buffer
Rasterize
Vertex
Fragment
CPU
Pixels
Texture/Buffer

## Slide 17: GPU graphics processing model
CPU
Displayed
Pixels
Vertex
Fragment
Rasterize
Z-Buffer
Texture/Buffer

## Slide 18: GPU Processing Model
SIMD for efficiency
  Same processors for vertex & pixel
SIMD Batches
  Limits on # of vertices & pixels that can run together
  Improve Utilization
  Limit divergence
Basic scheduling
  If batch of pixels, run it
  Otherwise run some vertices to make more

## Slide 19: NVIDIA Maxwell
[NVIDIA, NVIDIA GeForce GTX 980 Whitepaper, 2014]

## Slide 20: Maxwell SIMD Processing Block
32 Cores
8 Special Function Units (SFU)
  Double precision, trig, …
  Still issue 1/thread, but run ¼ rate
8 Load/Store memory access
  Hide latency by interleaving threads
Wave (AMD) / Warp (NVIDIA)
  One set of lanes (AMD) / threads (NVIDIA)
  Want at least 4-8 interleaved
  % of max = Occupancy

## Slide 21: GPU Registers
Scalar General Purpose Register (SGPR)
  Same value for all threads
  AMD term: Pixar’s Renderman (& GLSL) called these uniform
Vector General Purpose Registers (VGPR)
  Different value in every thread
  AMD term: Pixar & GLSL called these varying
  # wavefronts usually limited by VGPR

## Slide 22: Maxwell Streaming Multiprocessor (SMM)
4 SIMD blocks (128 total cores)
Share L1 Caches
Between-core shared memory
  Communication through this shared memory is fast
Share tessellation HW
  Hardware support for tessellation shaders

## Slide 23: Maxwell Graphics Processing Cluster (GPC)
4 SMM (512 total cores)
Share rasterizer

## Slide 24: Full NVIDIA Maxwell
4 GPC (2048 total cores)
Share L2
Share dispatch
  Decides which threads to launch and when

## Slide 25: NVIDIA Volta
[NVIDIA, NVIDIA TESLA V100 GPU ARCHITECTURE]