## Slide 1: Graphics Hardware
CMSC 435/634

## Slide 2: A Graphics Pipeline
Transform
Clip
Rasterize
Shade
Z-buffer
Vertex
Fragment
Triangle

## Slide 3: Computation and Bandwidth
307 GFLOPS
20.5 TFLOPS
7.2 GB/s
14.4 GB/s
2.6 TB/s Texture
106 GB/s Fragment
Vertex
Triangle
Fragment
Based on:
• 100 Mtri/sec (1.6M/frame@60Hz)
• 300 Mvert/sec
• 50 bytes vertex data (P,N,T,uv)
• 50 bytes interpolated
• 68 bytes fragment output
• 5x depth complexity
• 16 4-byte textures
• 1024 ops/vert
• 1024 ops/frag
• No caching
• No compression

## Slide 4: Data Parallel
Task
Task
Task
Task
Distribute
Merge

## Slide 5: Sort First
Vertex
Distribute objects by screen tile
Triangle
Fragment
Some pixels
Vertex
Triangle
Fragment
Vertex
Triangle
Fragment
Objects
Screen

## Slide 6: Sort Middle
Vertex
Distribute objects or vertices
Merge & Redistribute by screen location
Vertex
Vertex
Triangle
Fragment
Triangle
Fragment
Triangle
Fragment
Triangle
Fragment
Some pixels
Some objects
Objects
Screen

## Slide 7: Sort Last
Vertex
Triangle
Fragment
Distribute by object
Z-merge
Vertex
Triangle
Fragment
Vertex
Triangle
Fragment
Full Screen
Some objects
Objects
Screen

## Slide 8: Screen Subdivision
Tiled
Interleaved

## Slide 9: Graphics Processing Unit (GPU)
Sort Middle(ish)
Fixed-Function HW for clip/cull, raster, texturing, Z-test
Programmable stages
Commands in, pixels out

## Slide 10: Architecture: Latency
CPU: Make one thread go very fast
Avoid the stalls
  Branch prediction
  Out-of-order execution
  Memory prefetch
  Big caches
GPU: Make 1,000,000 threads go very fast
Hide the stalls
  HW thread scheduler
  Swap threads to hide stalls

## Slide 11: Architecture (MIMD vs SIMD)
MIMD (CPU-Like)
SIMD (GPU-Like)
Flexibility
Horsepower
Ease of Use
(AMD K10 chip-architect.org)
(NVIDIA Volta / wikichip.org)
Actual computational Units

## Slide 12: SIMD Branching
if( x ) // mask threads
{
// issue instructions
}
else // invert mask
{
// issue instructions
} // unmask
Threads agree
or
Threads disagree
THEN

## Slide 13: SIMD Looping
while(x) // update mask
{
// do stuff
}
Everyone runs as long as slowest
Active
Inactive
% Active = Utilization
This example: 36% utilization

## Slide 14: GPU graphics processing model
Z-Buffer
Rasterize
Vertex
Fragment
CPU
Pixels
Texture/Buffer

## Slide 15: NVIDIA GeForce 6
[Kilgaraff and Fernando, GPU Gems 2]
Vertex
Rasterize
Fragment
Z-Buffer
Displayed
Pixels
Sort

## Slide 16: GPU graphics processing model
Z-Buffer
Rasterize
Vertex
Fragment
CPU
Pixels
Texture/Buffer

## Slide 17: GPU graphics processing model
CPU
Displayed
Pixels
Vertex
Fragment
Rasterize
Z-Buffer
Texture/Buffer

## Slide 18: GPU Processing Model
SIMD for efficiency
  Same processors for vertex & pixel
SIMD Batches
  Limits on # of vertices & pixels that can run together
  Improve utilization
  Limit divergence
Basic scheduling
  If batch of pixels, run it
  Otherwise run some vertices to make more

## Slide 19: NVIDIA Maxwell
[NVIDIA, NVIDIA GeForce GTX 980 Whitepaper, 2014]

## Slide 20: Maxwell SIMD Processing Block
32 Cores
8 Special Function Units (SFU)
  Double precision, trig, …
  Still issue 1/thread, but run ¼ rate
8 Load/Store memory access
  Hide latency by interleaving threads
Wave/Warp (AMD/NVIDIA)
  One set of lanes/threads (AMD/NVIDIA)
  Want at least 4-8 interleaved
  % of max = Occupancy

## Slide 21: GPU Registers
Scalar General Purpose Register (SGPR)
  Same value for all threads
  Pixar’s Renderman (& GLSL) called these uniform
Vector General Purpose Registers (VGPR)
  Different value in every thread
  Pixar & GLSL called these varying
  # wavefronts usually limited by VGPR

## Slide 22: Maxwell Streaming Multiprocessor (SMM)
4 SIMD blocks (128 total cores)
Share L1 Caches
Between-core shared memory
  Communication through this shared memory is fast
Share tessellation HW
  Hardware support for tessellation shaders

## Slide 23: Maxwell Graphics Processing Cluster (GPC)
4 SMM (512 total cores)
Share rasterizer

## Slide 24: Full NVIDIA Maxwell
4 GPC (2048 total cores)
Share L2
Share dispatch
  Decides which threads to launch and when

## Slide 25: What’s new?
NVIDIA Maxwell was 12 years ago

## Slide 26: NVIDIA Blackwell
[NVIDIA, NVIDIA RTX Blackwell GPU Architecture, 2025]
More cores!!!!!

## Slide 27: Blackwell GPC

## Slide 28: Blackwell SM
Same number of SM registers and cores
Half the memory units
Fewer spec. func. Units
Add hardware for AI
  Matrix multiply, convolution
  FP16, FP6, FP4
Add ray tracing HW
  shared per SM