## Slide 1: Light & Displays
CMSC 435/634

## Slide 2: Light & Color

## Slide 3: Light
Electromagnetic wave
  E & M ⟂ to each other & direction of travel
Photon wavelength l, frequency f = c/l Photon energy q = h f = h c/l (in J)
  Visibile l ≈ 380 nm (blue) to 720 nm (red)
  c = speed of light, h = Planck’s constant
Spectral energy Q = J/nm

## Slide 4: Light
Infinite-dimensional function vector space
  spectrum(l)
  Dimensions = wavelength
Shine two lights on something adds energies
  Vector/Vector addition
Scale light energy, scales the intensity
  Scalar/Vector multiplication

## Slide 5: Radiometric Units
Term | Symbol | Units
Spectral Energy | Q | J
Spectral Power |  = dQ/dt | W = J/s
Irradiance | E = d/dA | W/m2
Radiant Intensity | I = d/d | W/sr
Radiance | L = d2/(d dA) | W/(sr m2)
/nm dropped by graphics convention

## Slide 6: Radiant Energy (Q)
Total energy (Joules)
Over all time, directions, area, …

## Slide 7: Radiant Flux ()
 = dQ/dt in Watts = J/s
Radiant energy per unit time
This is the one you probably want
  Unless you are measuring total energy absorbed
  E.g. by a plant over hours of daylight
Not the same as light bulb Watts
  Power in vs. power out

## Slide 8: Radiant Intensity (I)
I = d/d in W/sr
Radiant Flux emitted/received per unit solid angle
  Light from a point in a small cone of directions
Same units for incoming and outgoing light

## Slide 9: Radiosity (B)
B = d/dA in W/m2
All light leaving a patch of surface
  Emitted or reflected
  All directions at each point
  Measured per unit area

## Slide 10: Irradiance (E)
E = d/dA in W/m2
All light entering a patch of surface
  All directions at each point
  Measured per unit area

## Slide 11: Radiance (L)
L = d2/(d dA) in W/(sr m2)
Light entering patch of surface from a small range of directions
  Per unit area
  Per unit solid angle
Compare to Irradiance (over all directions)

## Slide 12: Spectral Graphs
A = Incandescent light
D = Daylight (50=horizon, 65=noon)
F = Fluorescent light

## Slide 13: Physiology
Rods
  active at low light levels (scotopic vision)
  only one wavelength sensitivity function
Cones
  active at normal light levels
  three types: sensitivity functions with different peaks

## Slide 14: Color Perception

## Slide 15: Color Perception
Cones = function dot product
For quantized spectra:
Projects to a 3D subspace

## Slide 16: Metamers
Different spectrum, looks the same
Same 3D projection

## Slide 17: Color Basis
Can transform to any 3D linear basis
  As long as it spans the same subspace
Transform between bases with a 3x3 matrix

## Slide 18: Linear Bases
Additive (light)
  Tristimulus (LMS cone response)
  CIE XYZ (from color matching experiments)
  RGB (red/green/blue; different for each device)
  Yuv, YCrCb, … (intensity/2 chroma)
Subtractive (pigment)
  CMY = 1 - RGB (cyan/magenta/yellow)
    grade school Blue, Red, Yellow
  CMYK (cyan/magenta/yellow/black)
    Hard to reliably get pure black in ink by mixing CMY

## Slide 19: Chromaticity
Normalize x = X / (X+Y+Z); y = Y / (X+Y+Z)

## Slide 20: RGB Gamut
Gamut = representable colors

## Slide 21: Subtractive
Start at white, remove R, G, or B

## Slide 22: White Points & Color Temperature
Color of radiating black body at given temperature (°K)
Color of a black body that temperature, not necessarily the temperature of the light

## Slide 23: Nonlinear Color Spaces
HSV: Cylindrical Coordinates
  Hue = angle
  Saturation = distance from central axis
  Value = distance along axis
Related HLS
  Hue/Lightness/Saturation

## Slide 24: Perception

## Slide 25: Nonlinear Perception
Linear colors don’t look uniformly different
Nonlinear Luminance
  Gamma (sRGB), L*uv
Nonlinear Luminance & Color
  L*u*v*, L*a*b*
  Can measure color distances

## Slide 26: Gamma
Gamma transform
  sRGB is approximately with linear bit near 0
Images
  Often stored with sRGB or gamma
  Nonlinear colors do not add
    Undo gamma, operate in linear space, redo gamma
Some games use

## Slide 27: Photometric Units
Visual intensity
Term | Symbol | Units
Luminous Energy | Q | talbot
Lumens |  = dQ/dt | lm = talbot/s
Illuminance (lux) | E = d/dA | lx = lm/m2
Candelas | I = d/d | cd = lm/sr
Luminance (nit) | L = d2/(d dA) | nt = cd/m2

## Slide 28: Dynamic Range
Real world: High Dynamic range (HDR)
  Outside, moonlight 0.0014 nt
  Outside, sunrise 25 nt
  Outside, overcast 700 nt
  Outside, sunlight 5,000 nt
  Sky 7,000 nt
  Light blub 130,000 nt
  Sun 1,600,000,000 nt
Displays: Low Dynamic Range (LDR)
  Typically about 1 nt to 250 nt

## Slide 29: Tone Mapping
HDR ∈ [0,∞); LDR ∈ [0,1] or [0,255]
Convert HDR to LDR
  Nonlinear tone mapping curve
  Adapt to overall intensity
  Time-dependent adaptation