## Slide 1: CMSC 491/691
Sampling and Antialiasing

## Slide 2: Vectors and Functions
Vector | Discrete | Continuous
V | V[I] | V(x)
a V + b U | a V[I] + b U[I] | a V(x) + b U(x)
V • U | ∑ V[I] U*[I] | ∫ V(x) U*(x) dx

## Slide 3: Vectors and Functions
2t projected onto 1, t, t2
2t
1
t
t2

## Slide 4: Function Bases
Time: d(t)
Polynomial / Power Series: tn
Discrete Fourier: ei π t K/N / √2N
  K, N integers
  t, K  [-N, N]
  (where eiq = cos q + i sin q)
Continuous Fourier: ei w t / √2π

## Slide 5: Fourier Transforms
 | Discrete Time | Continuous Time
Discrete Frequency | Discrete Fourier Transform | Fourier Series
Continuous Frequency | Discrete-time Fourier Transform | Fourier Transform

## Slide 6: Convolution
f(t) g(t)  F(w) ＊ G(w)
g(t) ＊ f(t)  F(w) G(w)
Where f(t) ＊ g(t) = ∫ f(s) g(t-s) ds
  Dot product with shifted kernels

## Slide 7: Filtering
Filter in frequency domain
  FT signal to frequency domain
  Multiply signal & filter
  FT signal back to time domain
Filter in time domain
  FT filter to time domain
  Convolve signal & filter

## Slide 8: Sampling
Multiply signal by pulse train

## Slide 9: Reconstruction
Convolve samples & reconstruction filter
Sum weighted kernel functions

## Slide 10: Aliasing
High frequencies alias as low frequencies

## Slide 11: Aliasing in images

## Slide 12: Antialiasing
Blur away frequencies that would alias
Blur preferable to aliasing
Filter kernel size
  IIR = infinite impulse response
  FIR = finite impulse response
    Windowed filters

## Slide 13: “Ideal” Sinc
Low pass filter eliminates all high freq
  box in frequency domain
    Gets rid of all (& only) aliasing frequencies
  sinc in spatial domain (sin x / x)
    Possible negative results
    Ringing
    Infinite kernel
Exact reconstruction to Nyquist limit
  Sample frequency ≥ 2x highest frequency
  Exact only if reconstructing with ideal low-pass filter (=sinc)

## Slide 14: Graphics Kernels: Spatial Box
Easy to implement
Sinc in frequency domain
Significant residual aliasing
Really pretty bad quality

## Slide 15: Graphics Kernels: Gaussian
Wide Image Gaussian → Narrow Frequency Gaussian
Narrow Image Gaussian → Wide Frequency Gaussian
Mostly zero a few standard deviations out
  Window to make finite
Can over-blur
→

## Slide 16: Graphics Kernels: Mitchell
Class of cubic filters
Mitchell & Netravalli, Reconstruction Filters in Computer Graphics, SIGGRAPH 1988
Recommend B=C=1/3

## Slide 17: Graphics Kernels: Lanczos
Windowed sinc
  Windowed by central lobe of a wider sinc
  Class by how many lobes
Lanczos-2 is popular

## Slide 18: Filtering & Reconstruction
Ideal Continuous Image
Sample
Reconstruction Filter
Sampled Image Pixels
Continuous Display

## Slide 19: Filtering, Sampling, Reconstruction
Filtered Continuous Image
Ideal Continuous Image
Sampled Image Pixels
Continuous Display
Filter
Sample
Reconstruction Filter

## Slide 20: Combine Filter & Sample
Can combine filter and sample
  Evaluate convolution at samples
Ideal Continuous Image
Sampled Image Pixels
Continuous Display
Sampling Filter
Reconstruction Filter

## Slide 21: Analytic Area Sampling
Compute “area” of pixel covered
Box in spatial domain
  Nice finite kernel
    easy to compute
  sinc in freq domain
    Plenty of high freq
    still aliases

## Slide 22: Analytic higher order filtering
Fold better filter into rasterization
  Can make rasterization much harder
  Usually just done for lines
    Draw with filter kernel “paintbrush”
Only practical for finite filters

## Slide 23: Supersampling
Numeric integration of filter
Grid with equal weight = box filter
Push up Nyquist frequency
  Edges: ∞ frequency, still alias
Other filters:
  Grid with unequal weights
  Priority sampling

## Slide 24: Adaptive sampling
Vary numerical integration step
More samples in high contrast areas
Easy with ray tracing, harder for others
Possible bias

## Slide 25: Stochastic sampling
Monte-Carlo integration of filter
Sample distribution
  Poisson disk
  Jittered grid
Aliasing  Noise

## Slide 26: Common Antialiasing Techniques
SSAA
MSAA
MLAA / FXAA
TAA

## Slide 27: SSAA: Supersampled Antialiasing
Render higher resolution
  N x per-pixel rasterization samples
  N x pixel shading samples
  N x buffer sizes
Filter & resample
N-sample

## Slide 28: MSAA: Multisample Antialiasing
N-sample rasterization and visibility, only shade one
  N x per-pixel rasterization samples
  1 x pixel shading samples
  1 x buffer sizes
Hardware support, including sample placement

## Slide 29: MLAA: Morphological Antialiasing
Postprocessing pass on aliased image
  1 x per-pixel rasterization samples
  1 x pixel shading samples
  1 x buffer sizes
Algorithm
  Look for jaggy edges
  Infer original edges
  “Fix” image
FXAA is a popular variant
  Available shading code

## Slide 30: TAA: Temporal Antialiasing
Share samples across frames
  N x rasterization samples (1 per frame)
  N x shading samples (1 per frame)
  2 x buffer sizes (add history buffer)
Exponential weighted average
Must find previous data for “this” pixel in history

## Slide 31: Exponential Average
Regular average
Incremental average

## Slide 32: Exponential Average
Incremental
Exponential: don’t change weight

## Slide 33: History
Account for motion
  Camera motion: current and previous transform
  Object motion: velocity buffer
    Also useful for motion blur
Resampling
  Land between pixels
  Avoid blurring history data
Rejection
  Occlusion, Disocclusion = stuff in buffer may be a different object
  Color clamping

## Slide 34: TAA problems
Start-up aliasing
  Alias until you get enough samples
Disocclusion aliasing
  No history when things appear
Ghosting
  Rejection/clamping failure on noisy backgrounds
Pulsing
  Cycle of reject/average
Fireflies
  Single bright sample hard to antialias

## Slide 35: TAA wins
Monte Carlo all the things
  Some samples per frame
  Multiply by TAA
Screen Space Reflection
  1-12 samples per pixel * 8 frames ≈ 8-96 samples
Ambient Occlusion
  1-6 samples per pixel * 8 frames ≈ 8-42 samples
Percentage Closer Soft Shadows
  32 samples per pixel * 4 pixels/quad * 8 frames = 1024 samples

## Slide 36: Resampling
Resampled Image Pixels
Continuous Image
Reconstruction Filter
Sampling Filter
Image Pixels

## Slide 37: Resampling
Resampled Image Pixels
Resampling Filter
Image Pixels

## Slide 38: Resampling with less blur
Samples → continuous image = diffusion
What samples at the new rate give the same continuous image?
Solution
  Laplacian ≈ Difference of Gaussians ≈ Unsharp Mask ≈ Lanczos 2 ≈ Mitchell
  All same shape and width
UE4 mostly uses 5-sample Mitchell