## Slide 1: Graphics Hardware
UMBC Graphics for Games

## Slide 2: CPU Architecture
Start 1-4 instructions per cycle
Pipelined, takes 8-16 cycles to complete
Memory is slow
  1 cycle for registers ~20
  2-4 cycles for L1 cache ~22
  10-20 cycles for L2 cache ~24
  50-70 cycles for L3 cache ~26
  200-300 cycles for memory ~28

## Slide 3: CPU Goals
Make one thread go very fast
  Avoid pipeline stalls
Branch prediction
  Misprediction up to 64 instruction penalty
Out-of-order execution
  Don’t wait for one instruction to finish before starting others
Memory prefetch
  Recognize access patterns, get data to fast levels of cache early
Big caches
  Though bigger caches add latency

## Slide 4: CPU Performance Tips
Avoid unpredictable branches
  Specialize code
  Avoid virtual functions when possible
  Sort similar cases together
Avoid caching data you don’t use
  Core of data oriented design
Avoid unpredictable access
  O(n) linear search faster than O(log n) binary up to 50-100 elements
    Linear access = can prefetch; branch predictable until final found it iteration
  For small numbers, constants matter
  Don’t underestimate how big small numbers can be

## Slide 5: GPU Goals
Make 1000’s of threads running the same program go very fast
  Hide stalls
Share hardware
  All running the same program
Swap threads to hide stalls
  Large, flexible register set
  Enough for active and stalled threads

## Slide 6: Architecture (MIMD vs SIMD)
CTRL
ALU
ALU
CTRL
ALU
ALU
CTRL
CTRL
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
MIMD (CPU-Like)
SIMD (GPU-Like)
CTRL
Flexibility
Horsepower
Ease of Use

## Slide 7: SIMD Branching
if( x ) // mask threads
  // issue instructions
else // invert mask
// issue instructions
// unmask
Threads agree, issue if
Threads disagree, issue if AND else
Threads agree, issue else

## Slide 8: SIMD Looping
while(x) { // update mask
// do stuff
}
They all run ‘till the last one’s done….
Useful
Useless
% Useful = Utilization

## Slide 9: GPU graphics processing model
CPU
Displayed
Pixels
Vertex
Geometry
Fragment
Rasterize
Z-Buffer
Texture/Buffer

## Slide 10: NVIDIA Maxwell
[NVIDIA, NVIDIA GeForce GTX 980 Whitepaper, 2014]

## Slide 11: Maxwell SIMD Processing Block
32 Cores
8 Special Function
One set of threads
  NVIDIA: Warp, AMD: Wavefront
  Want at least 4-8 interleaved
  % of max = Occupancy
Flexible Registers
  Vector General Purpose Registers (VGPR)
    AMD term: Different value at each core
  # warps usually limited by registers

## Slide 12: Maxwell Streaming Multiprocessor (SMM)
4 SIMD blocks
Share L1 Caches
Share memory
Share tessellation HW

## Slide 13: Maxwell Graphics Processing Cluster (GPC)
4 SMM
Share raster

## Slide 14: Full NVIDIA Maxwell
4 GPC
Share L2
Share dispatch

## Slide 15: NVIDIA Volta
[NVIDIA, NVIDIA TESLA V100 GPU ARCHITECTURE]

## Slide 16: GPU Performance Tips

## Slide 17: Graphics System Architecture
Your Code
API
Driver
Current Frame
(Buffering Commands)
Previous Frame(s)
(Submitted, Pending Execution)
GPU
Produce
Consume
GPU
GPU(s)
Display

## Slide 18: GPU Performance Tips: Communication
Reading Results Derails the train…..
  Occlusion Queries → Death
    When used poorly: don’t ask for the answer for 2-3 frames
  Framebuffer reads → DEATH!!!
    Almost always…
CPU-GPU communication should be one way
  If you must read, do it a few frames later…

## Slide 19: GPU Performance Tips: API & Driver
Minimize shader/texture/constant changes
  Flush pipeline, change state, restart
Minimize Draw calls
  One instanced draw is much more efficient than many static draws
Minimize CPU → GPU traffic
  Use static vertex / index buffers if you can
  Use dynamic buffers if you must
    With discarding locks: region being used, region in queue, region being updated

## Slide 20: GPU Performance Tips: Shaders
NO unnecessary work!
  Precompute constant expressions
  Divide by constant → Multiply by reciprocal
    Use x*(1./3.) vs. x/3.
    Not always the same in float math, compiler is not allowed to make that optimization
Minimize fetches
  Prefer compute (generally)
  If ALU/TEX < 4+, ALU is under-utilized
  If combining static textures, bake it all down…

## Slide 21: GPU Performance Tips: Shader Occupancy
Know what’s limiting you
  Occupancy only helps when stall limited (typically memory stalls)
  Often VGPR limited
  Could be local/shared memory
Limit VGPR usage by specializing shaders
Limit VGPR usage with computation that’s constant across the warp

## Slide 22: GPU Performance Tips: Shaders
Careful with flow control
  Avoid divergence
  Flatten small branches
  Prefer simple control structure
  Specialize shader (though can lead to 1000’s of shaders)
Double-check the compiler
  Shader compilers are getting better…
Look over artists’ shoulders
  Material editors give them lots of rope….

## Slide 23: GPU Performance Tips: Vertices
Use the right data format
  Cache-optimized index buffer
  Small, 16-byte aligned vertices
Cull invisible geometry
  Coarse-grained (few thousand triangles) is enough
  “Heavy” Geometry load is ~2MTris and rising

## Slide 24: GPU Performance Tips: Pixels
Small triangles hurt performance
  GPU always renders 2x2 pixel blocks (for texture filtering)
  Renders extra “fake” pixels to fill block → Waste at triangle edges
Respect the texture cache
  Adjacent pixels should touch same or adjacent texels
  Use the smallest possible texture format
  Avoid incoherent texture reads
Do work per vertex
  There’s usually less of those (see small triangles)

## Slide 25: GPU Performance Tips: Pixels
HW is very good at Z culling
  Early Z, Hierarchical Z
If possible, submit geometry front to back
“Z Priming” is commonplace (UE4 does this)
  Render with simple shader to z-buffer
  Then render with real shader
  Helps a ton for complex forward shaders, but useful even for g-buffer

## Slide 26: GPU Performance Tips: Frame Buffer
Turn off what you don’t need
  Alpha blending
  Color/Z writes
Minimize redundant passes
  Multiple lights/textures in one pass
  As long as it doesn’t kill your occupancy
Use the smallest possible pixel format
Consider clip/discard in transparent regions
  Throws out pixels

## Slide 27: GPU Performance Tips: Overall
Learn as much as possible about GPU internals
  Use that to guide your optimization decisions
Benchmark, don’t assume
  Complex interrelationships can surprise you
  Build a good A/B test timing framework
Do at least big-picture optimizations early