## Slide 1: Graphics Hardware
UMBC Graphics for Games

## Slide 2: CPU Architecture
Start 1-4 instructions per cycle
Pipelined, takes 8-16 cycles to complete
Memory is slow
  1 cycle for registers ~20
  2-4 cycles for L1 cache ~22
  10-20 cycles for L2 cache ~24
  50-70 cycles for L3 cache ~26
  200-300 cycles for memory ~28

## Slide 3: CPU Goals
Make one thread go very fast
  Avoid pipeline stalls
Branch prediction
  Misprediction up to ~64 instruction penalty
Out-of-order execution
  Don’t wait for one instruction to finish before starting others
Memory prefetch
  Recognize access patterns, get data to fast levels of cache early
Big caches
  Though bigger caches add latency

## Slide 4: CPU Performance Tips
Avoid unpredictable branches
  Specialize code
  Avoid virtual functions when possible
  Sort similar cases together
Avoid caching data you don’t use
  Core of data oriented design / Structure of Arrays organization
Avoid unpredictable access
  O(N) linear search faster than O(log N) binary up to 50-100 elements
    Linear access = can prefetch; branch predictable until final found it iteration
  Asymptotically worse, but for small N, constants matter
  Don’t underestimate how big small N can be

## Slide 5: GPU Goals
Make 1000’s of threads running the same program go very fast
  Hide stalls
Share hardware
  All running the same program
Swap threads to hide stalls
  Large, flexible register set
  Enough for active and stalled threads

## Slide 6: Architecture (MIMD vs SIMD)
CTRL
ALU
ALU
CTRL
ALU
ALU
CTRL
CTRL
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
MIMD (CPU-Like)
SIMD (GPU-Like)
CTRL
Flexibility
Horsepower
Ease of Use

## Slide 7: SIMD Branching
if( x ) // mask threads
{
// issue instructions
}
else // invert mask
{
// issue instructions
} // unmask
Threads agree, issue if
Threads disagree, issue if THEN else
Threads agree, issue else

## Slide 8: SIMD Looping
while(x) // update mask
{
// do stuff
}
They all run ‘till the last one’s done….
Useful
Useless
% Useful = Utilization

## Slide 9: GPU Programming Model
Geometry
Pixel
Texture/Buffer
Rasterize
Vertex
Displayed Pixels
Z-buffer/ Blend

## Slide 10: GPU Processing Model
Z-buffer/ Blend
Texture/Buffer
Displayed Pixels
Rasterize
Primitive
Assembly
Pixel
Geometry
Vertex
Sampler

## Slide 11: NVIDIA Maxwell
[NVIDIA, NVIDIA GeForce GTX 980 Whitepaper, 2014]

## Slide 12: Maxwell SIMD Processing Block
32 Cores
One set of threads
  Warp (NVIDIA), Wavefront (AMD)
  Want at least 4-8 interleaved
  % of max = Occupancy
8 Load/Store memory access
  Hide latency by interleaving threads
8 Special Function
  Double precision, trig, …
  Still issue 1/thread, but run ¼ rate

## Slide 13: GPU Registers
Scalar General Purpose Register (SGPR)
  Same value for all threads
  AMD term, Pixar’s Renderman (& GLSL) called these uniform
Vector General Purpose Registers (VGPR)
  Different value in every thread
  AMD term, Pixar & GLSL called these varying
  # wavefronts usually limited by VGPR

## Slide 14: Maxwell Streaming Multiprocessor (SMM)
4 SIMD blocks
Share L1 Caches
Share memory
  Communication through this shared memory is fast
Share tessellation HW

## Slide 15: Maxwell Graphics Processing Cluster (GPC)
4 SMM
Share rasterizer

## Slide 16: Full NVIDIA Maxwell
4 GPC
Share L2
Share dispatch
  Decides which threads to launch and when

## Slide 17: NVIDIA Volta
[NVIDIA, NVIDIA TESLA V100 GPU ARCHITECTURE]

## Slide 18: Care and Feeding of a GPU

## Slide 19: Parallel Submission
OpenGL and DX11 had a 1-CPU thread bottleneck to the GPU
DX12, Vulkan and Metal are designed for multiple CPU cores to simultaneously submit work to a single GPU
Build a Command List, submit to GPU when ready
Command List includes all necessary state, can execute in any order
Tell GPU about resource dependencies (Barriers / Transitions)
  Enforces partial ordering of command list execution

## Slide 20: Resource Transitions
What kind of memory operations does this buffer need to support?
  (CPU/GPU) (read/write) (once/many times)
  CPU write once, GPU read once; GPU write once, GPU read many times; …
Source/Target stage for the transition
  When is it ready? When will it be used?
What use should it be optimized for?
  CPU staging, Texture, Render Target, Depth Buffer, Vertex Buffer, Index Buffer, Graphics read/write unordered access view (UAV), Compute buffer, …
Explicitly transition between these
  E.g. between render target write in pass A and texture read in pass B

## Slide 21: Setting up a Command List
What do I write?
  Render Targets, UAVs
  Transition to make sure anyone reading them is done
What do I read?
  Transition if just written or in a different format
What shader(s) am I using?
What shader parameter blocks?
  Given by Descriptors & Root Signature

## Slide 22: Setting up a Graphics Command List
Begin Pass / End Pass
  Primarily necessary for batching on mobile
Rendering Graphics Pipeline State Object (PSO)
  Primitive Type: triangle list, fan, strip, quad, points, …
  Rasterizer State: Solid/wire frame, two sided / CW side / CCW side, MSAA
  Depth/Stencil State: Comparison (<, ≤,=,≠, ≥, >), update?
  Blend State: 𝛼 * new + (1 - 𝛼) * old
    Generalize to (a * new (op) b * old) for limited selection of a, b, and (op)

## Slide 23: GPU Performance Tips

## Slide 24: Graphics System Architecture
Your Code
API
Driver
Current Frame
(Buffering Commands)
Previous Frame(s)
(Submitted, Pending Execution)
GPU
Produce
Consume
GPU
GPU(s)
Display

## Slide 25: GPU Performance Tips: Communication
Reading Results Derails the train…..
  Occlusion Queries → Death
    When used poorly: don’t ask for the answer for 2-3 frames
  Framebuffer reads → DEATH!!!
    Almost always…
CPU-GPU communication should be one way
  If you must read, do it a few frames later…

## Slide 26: GPU Performance Tips: API & Driver
Minimize shader/texture/constant changes
  Flush pipeline, change state, restart
Minimize Draw calls
  One instanced draw is much more efficient than many static draws
Minimize CPU → GPU traffic
  Use static vertex / index buffers if you can
  Use dynamic buffers if you must
    With discarding locks: region being used, region in queue, region being updated

## Slide 27: GPU Performance Tips: Shaders
NO unnecessary work!
  Precompute constant expressions
  Divide by constant → Multiply by reciprocal
    Use x*(1./3.) vs. x/3.
    Not always the same in float math, compiler is not allowed to make that optimization
Minimize fetches
  Prefer compute (generally)
  If ALU/TEX < 4+, ALU is under-utilized
  If combining static textures, bake it all down…

## Slide 28: GPU Performance Tips: Shader Occupancy
Know what’s limiting you
  Occupancy only helps when stall limited (typically memory stalls)
  Often VGPR limited
  Could be local/shared memory
Limit VGPR usage by specializing shaders
  In UE4, ifdefs in shaders
Limit VGPR usage with computation that’s constant across the warp

## Slide 29: GPU Performance Tips: Shaders
Careful with flow control
  Avoid divergence
  Flatten small branches
  Prefer simple control structure
  Specialize shader (though can lead to 1000’s of shaders)
Double-check the compiler
  Shader compilers are getting better…
Look over artists’ shoulders
  Material editors give them lots of rope….

## Slide 30: GPU Performance Tips: Vertices
Use the right data format
  Cache-optimized index buffer
  Small, 16-byte aligned vertices
Cull invisible geometry
  Coarse-grained (few thousand triangles) is enough
  “Heavy” Geometry load is ~2MTris and rising

## Slide 31: GPU Performance Tips: Pixels
Small triangles hurt performance
  GPU always renders 2x2 pixel blocks (for texture filtering)
  Renders extra “fake” pixels to fill block → Waste at triangle edges
Respect the texture cache
  Adjacent pixels should touch same or adjacent texels
  Use the smallest possible texture format
  Avoid incoherent texture reads
Do work per vertex
  There’s usually less of those (see small triangles)

## Slide 32: GPU Performance Tips: Pixels
HW is very good at Z culling
  Early Z, Hierarchical Z
If possible, submit geometry front to back
“Z Priming” is commonplace (UE4 does this)
  Render with simple shader to z-buffer
  Then render with real shader
  Helps a ton for complex forward shaders, but useful even for g-buffer

## Slide 33: GPU Performance Tips: Frame Buffer
Turn off what you don’t need
  Alpha blending
  Color/Z writes
Minimize redundant passes
  Multiple lights/textures in one pass
  As long as it doesn’t kill your occupancy
Use the smallest possible pixel format
Consider clip/discard in transparent regions
  Throws out pixels

## Slide 34: GPU Performance Tips: Overall
Learn as much as possible about GPU internals
  Use that to guide your optimization decisions
Benchmark, don’t assume
  Complex interrelationships can surprise you
  Build a good A/B test timing framework
Do at least big-picture optimizations early