## Slide 1: Multipass Rendering
UMBC Graphics for Games

## Slide 2: Multiple passes
Render geometry
Render again
  Different geometry
  Same geometry over again

## Slide 3: Reasons for multiple passes
Non-local in space
  Information from other pixels
  Information from other views
Non-local in time
  Information that otherwise would not be computed yet
  Information from previous frames
Changes in representation
  Higher or lower resolution rendering
Algorithmically convenient

## Slide 4: Forward Rendering

## Slide 5: One triangle at a time
Transform
  Where do the vertices land on the screen
Rasterize
  Which pixels are in the triangle
Shade
  What color is it
Visibility
  Z value per pixel, is this pixel closer?
Blend
  Replace color or blend with existing color

## Slide 6: Early Z Optimization
Keep farthest Z in each 2x2, 4x4, 16x16, etc. block of pixels
  Update as you go
If all 3 vertices are further than that, don’t even rasterize
aa
Have to draw
Don’t have to draw
Have to draw
Don’t have to draw
View direction
Notes: Change View Mode from Lit to Buffer Visualizations > Scene Depth to see the depths (can’t directly see the hierarchical depths, since they’re in the GPU)

## Slide 7: Z pre-pass
Worst case, rendering back to front, get no benefit from early Z
For best early Z performance, sort opaque stuff front to back
  O(n log n)
Instead, render just depths of opaque stuff first
  Two O(n) passes
  Perfect early Z

## Slide 8: Shadow Map
Is the point I’m shading closer to the light than anything else?
Render depths as seen from the light, keep the closest
  Image with closest depths = shadow map
  Non-local information from another view
View
Light
Notes: See representation of UE4’s shadow maps with console command “vis ShadowDepthAtlas uv1”, ”vis 0” to turn off.

## Slide 9: Reflection Map
What color would I see for a reflection in this direction
If far away, only the direction matters, not the reflection
  Render views from a representative location
  Use in final render
Notes: There’s a reflection capture node in the default level. Change view mode from “Lit” to “Reflections” to see.

## Slide 10: Deferred Rendering

## Slide 11: Shade once
Transform / Render / Visibility
  Render shading parameters to G-Buffers
  Sometimes called the base pass
Can do as part of Z pre-pass
  But also useful to do after to limit G-buffer write bandwidth
Result = depth and shading parameters at each pixel
  Depth and pixel X/Y enough to reconstruct 3D position
  Classic deferred shading: G-buffer for albedo, normal, texture coordinates, …
  Can also do triangle ID and location in triangle

## Slide 12: Shading pass
Draw a full-screen quad
  Shader uses pixel location, Z buffer, in G buffers
Can be more efficient to draw a single triangle instead
Or just use a compute shader

## Slide 13: Partial updates : point & spot lights
Render only light extents
  Check z-buffer, but don’t write it
  Pixels not covered can’t see the light
Also, tiles, depth culling
  Avoid computing lights in open space
Panagiotis Christopoulos Charitos, AnKi 3D Engine
Notes: When a light is selected in UE4, you see the influence shape. Drop a Point Light or Spot Light into a scene, then select it to see.

## Slide 14: Other pixel’s data : Motion blur
Per-pixel velocity
  Record object velocity during base pass
  Remember frame-to-frame view changes
Blur along a path backwards in that direction
  Look up other pixels data
Notes: Show > Visualize > Motion Blur to see a grid of motion vectors.
Shows camera motion. Can also add a Rotating Motion component to a shape, set the Pivot Translation for X to about 100 or so.

## Slide 15: Chained passes: Blur, bloom, lens flare
Need data from too many other pixels?
Compute hierarchically
  Pass: full to 1/4 resolution (1/2 in each dimension)
    Each pixel only looks at a local neighborhood
  Pass: 1/4 to 1/16 resolution
  Pass: 1/16 to 1/64 resolution
  …
Use one or more of these to compute final result
Or compute hierarchically on the way up: 1/64 → 1/16 → 1/4 → full
Notes: In console, do “vis BloomDownsample1 uv1” through ”vis BloomDownsample5 uv1” for computation pass
For reconstruction using it, “vis BloomBlurX@1 uv1” through “vis BloomBlurX@5 uv1” and “vis BloomBlurY@1 uv1” through “vis BloomBlurY@5 uv1”
The uv1 stretches to full screen, use uv2 to see the actual size of the buffer.

## Slide 16: Transparency pass
Forward rendering pass for transparent objects
  Use deferred depth: don’t draw behind already rendered opaque stuff
  Sort back-to-front
  Blend over whatever is already there
Notes: Drop at least one object in the scene and put a translucent material on it like “M_SimpleTranslucent”
In console: ”vis SceneColor uv1” to see the opaque stuff, “vis SeparateTranslucency uv1” to see just transparent stuff. “vis 0” to turn off
Also change view mode from Lit to Buffer Visualization > Separate Translucency RGB or Separate Translucency Alpha

## Slide 17: Temporal Antialiasing
Aliasing = jaggy artifacts
Fix with multiple samples per pixel
  Expensive!
Do some each frame, blend together
Notes: Show > Antialiasing to turn on and off to see with and without aliasing
In console, “vis SceneColor uv1” will show jittering of un-blended samples each frame

## Slide 18: Skin
Subsurface scattering
  Photons bounce around under skin surface
Approximate with blur
Render once, then blur
  Non-local information
Notes: Use engine material M_SkinBall. Switch View Mode from Lit to Buffer Visualizations > Subsurface Color

## Slide 19: Screen Space Reflection (SSR)
Reflections off of shiny surfaces require global knowledge
Approximate with pixel values already rendered
  Depth + color approximates scene
Trace rays through this data
Ray spread driven by gloss
Blend with TAA
Notes: Make a material with Specular = 1 and Roughness = about 0.2. Turn Show > Lighting Features > Screen Space Reflection on and off

## Slide 20: Screen Space Ambient Occlusion (SSAO)
Approximation for bounce light
What can the local surface see?
Use per-pixel depths of nearby pixels to approximate
Blend with TAA
Notes: Drop a couple of cubes into a scene so you’re looking at an inside corner like you’d see in the corner of a room. Make sure they’re positioned so the corner is lit (not shadowed).
Turn Show > Lighting Features > Screen Space Ambient Occlusion on and off