## Slide 1: CMSC 611: Advanced Computer Architecture
Performance
Some material adapted from Mohamed Younis, UMBC CMSC 611 Spr 2003 course slides
Some material adapted from Hennessy & Patterson / © 2003 Elsevier Science

## Slide 2: Response-time Metric
Maximizing performance means minimizing response (execution) time

## Slide 3: Designer’s Performance Metrics
Users and designers measure performance using different metrics
  Users: quotable metrics (GHz)
  Designers: program execution
Designer focuses on reducing the clock cycle time and the number of cycles per program
Many techniques to decrease the number of clock cycles also increase the clock cycle time or the average number of cycles per instruction (CPI)

## Slide 4: Example
A program runs in 10 seconds on a computer “A” with a 400 MHz clock.
We desire a faster computer “B” that could run the program in 6 seconds.
The designer has determined that a substantial increase in the clock speed is possible, however it would cause computer “B” to require 1.2 times as many clock cycles as computer “A”. What should be the clock rate of computer “B”?
To get the clock rate of the faster computer, we use the same formula

## Slide 5: Calculation of CPU Time
CPU time = Instruction count  CPI  Clock cycle time
Or

## Slide 6: CPU Time (Cont.)
CPU execution time can be measured by running the program
The clock cycle is usually published by the manufacture
Measuring the CPI and instruction count is not trivial
  Instruction counts can be measured by: software profiling, using an architecture simulator, using hardware counters on some architecture
  The CPI depends on many factors including: processor structure, memory system, the mix of instruction types and the implementation of these instructions

## Slide 7: CPU Time (Cont.)
Where: Ci is the count of number of instructions of class i executed
CPIi is the average number of cycles per instruction for that instruction class
n is the number of different instruction classes
Designers sometimes uses the following formula:

## Slide 8: Example
Suppose we have two implementation of the same instruction set architecture. Machine “A” has a clock cycle time of 1 ns and a CPI of 2.0 for some program, and machine “B” has a clock cycle time of 2 ns and a CPI of 1.2 for the same program. Which machine is faster for this program and by how much?
Both machines execute the same instructions for the program. Assume the number of instructions is “I”,
CPU clock cycles (A) = I  2.0 CPU clock cycles (B) = I  1.2
The CPU time required for each machine is as follows:
CPU time (A) = CPU clock cycles (A)  Clock cycle time (A)
= I  2.0  1 ns = 2  I ns
CPU time (B) = CPU clock cycles (B)  Clock cycle time (B)
= I  1.2  2 ns = 2.4  I ns
Therefore machine A will be faster by the following ratio:

## Slide 9: Comparing Code Segments
A compiler designer is trying to decide between two code sequences for a particular machine. The hardware designers have supplied the following facts:
For a particular high-level language statement, the compiler writer is considering two code sequences that require the following instruction counts:
Which code sequence executes the most instructions? Which will be faster? What is the CPI for each sequence?
Answer:
  Sequence 1: executes 2 + 1 + 2 = 5 instructions
  Sequence 2: executes 4 + 1 + 1 = 6 instructions 

## Slide 10: Comparing Code Segments
Sequence 1: CPU clock cycles = (2 1) + (1 2) + (2 3) = 10 cycles
Sequence 2: CPU clock cycles = (4 1) + (1 2) + (1 3) = 9 cycles
Therefore Sequence 2 is faster although it executes more instructions
Using the formula:
Sequence 1: CPI = 10/5 = 2
Sequence 2: CPI = 9/6 = 1.5
Using the formula:
Since Sequence 2 takes fewer overall clock cycles but has more
instructions it must have a lower CPI

## Slide 11: The Role of Performance
Hardware performance is a key to the effectiveness of the entire system
Performance has to be measured and compared to evaluate designs
To optimize the performance, major affecting factors have to be known
For different types of applications
  different performance metrics may be appropriate
  different aspects of a computer system may be most significant
Instructions use and implementation, memory hierarchy and I/O handling are among the factors that affect the performance

## Slide 12: Calculation of CPU Time
Where: Ci is the count of number of instructions of class i executed
CPIi is the average number of cycles per instruction for that instruction class
n is the number of different instruction classes

## Slide 13: Important Equations (so far)