## Slide 1: CMSC 611: Advanced Computer Architecture
Benchmarking
Some material adapted from Mohamed Younis, UMBC CMSC 611 Spr 2003 course slides
Some material adapted from Hennessy & Patterson / © 2003 Elsevier Science

## Slide 2: Important Equations (so far)

## Slide 3: Amdahl’s Law
A common theme in Hardware design is to make the common case fast
Increasing the clock rate would not affect memory access time
Using a floating point processing unit does not speed integer ALU operations
Example: Floating point instructions improved to run 2X; but only 34% of
actual instructions are floating point
Exec-Timenew = Exec-Timeold x (0.66 + .34/2) = 0.83 x Exec-Timeold
Speedupoverall = Exec-Timeold / Exec-Timenew = 1/0.83 = 1.205
The performance enhancement possible with a given improvement is limited by the amount that the improved feature is used

## Slide 4: Ahmdal’s Law Visually
notFP
notFP
FP
FP / S
Timeold
Timenew

## Slide 5: Ahmdal’s Law for Speedup

## Slide 6: Performance Benchmarks
Many widely-used benchmarks are small programs that have significant locality of instruction and data reference
Universal benchmarks can be misleading since hardware and compiler vendors do optimize their design for these programs
The best types of benchmarks are real applications since they reflect the end-user interest
Architectures might perform well for some applications and poorly for others
Compilation can boost performance by taking advantage of architecture-specific features
Application-specific compiler optimization are becoming more popular

## Slide 7: Comparing & Summarizing Performance
Wrong summary can present a confusing picture
  A is 10 times faster than B for program 1
  B is 10 times faster than A for program 2
Total execution time is a consistent summary measure
Relative execution times for the same workload
  Assuming that programs 1 and 2 are executing for the same number of times on computers A and B
Execution time is the only valid and unimpeachable measure of performance

## Slide 8: The SPEC Benchmarks
SPEC stands for System Performance Evaluation Cooperative suite of benchmarks
  Created by a set of companies to improve the measurement and reporting of CPU performance
SPEC2006 is the latest suite that consists of 12 integer (C or C++) and 17 floating-point (Fortran, C, and C++) programs
  Customized SPEC suites assess performance of graphics and transaction systems.
Since SPEC requires running applications on real hardware, the memory system has a significant effect on performance

## Slide 9: Effect of Compilation
App. and arch. specific optimization can dramatically impact performance

## Slide 10: Performance Reports
Guiding principle is reproducibility (report environment & experiments setup)

## Slide 11: The SPEC Benchmarks
Bigger numeric values of the SPEC ratio indicate faster machine
1997 “historical” reference machine

## Slide 12: SPEC95 for Pentium and Pentium Pro
The performance measured may be different on other Pentium-based hardware with different memory system and using different compilers
  At the same clock rate, the SPECint95 measure shows that Pentium Pro is 1.4-1.5 times faster while the SPECfp95 shows that it is 1.7-1.8 times faster
  When the clock rate is increased by a certain factor, the processor performance increases by a lower factor

## Slide 13: Performance Summary
Weighted arithmetic means summarize performance while tracking exec. time
Never use AM for normalizing time relative to a reference machine
Where: n is the number of programs executed
wi is a weighting factor that indicates the frequency of executing program i
with and

## Slide 14: Performance Summary (Cont.)
Geometric mean is suitable for reporting average normalized execution time
Where: n is the number of programs executed
With

## Slide 15: Price-Performance Metric
SPECbase CINT2000
SPEC CINT2000 per $1000 in price
Different results are obtained for other benchmarks, e.g. SPEC CFP2000
With the exception of the Sunblade price-performance metrics were consistent with performance
Prices reflects those of July 2001

## Slide 16: Historic Perspective
In early computers most instructions of a machine took the same execution time
  The measure of performance for old machines was the time required performing an individual operation (e.g. addition)
New computers have diverse set of instructions with different execution times
  The relative frequency of instructions across many programs was calculated
  The average instruction execution time was measured by multiplying the time of each instruction by its frequency
The average instruction execution time was a small step to MIPS that grew in popularity

## Slide 17: Using MIPS
The use of MIPS is simple and intuitive, faster machines have bigger MIPS
MIPS = Million of Instructions Per Second
  one of the simplest metrics
  valid only in a limited context
There are three problems with MIPS:
  MIPS specifies the instruction execution rate but not the capabilities of the instructions
  MIPS varies between programs on the same computer
  MIPS can vary inversely with performance (see next example)

## Slide 18: Example
Consider the machine with the following three instruction classes and CPI:
Now suppose we measure the code for the same program from two different compilers and obtain the following data:
Assume that the machine’s clock rate is 500 MHz. Which code sequence will execute faster according to MIPS? According to execution time?
Answer:
Using the formula:
Sequence 1: CPU clock cycles = (5 1 + 1 2 + 1 3)  109 = 10109 cycles
Sequence 2: CPU clock cycles = (10 1 + 1 2 + 1 3)  109 = 15109 cycles

## Slide 19: Example (Cont.)
Sequence 1: Execution time = (10109)/(500106) = 20 seconds
Sequence 2: Execution time = (15109)/(500106) = 30 seconds
Therefore compiler 1 generates a faster program
Using the formula:
Using the formula:
Sequence 1:
= 350
Sequence 2:
= 400
Although compiler 2 has a higher MIPS rating, the code from generated by compiler 1 runs faster