## Slide 1: CMSC 611: Advanced Computer Architecture
Pipelining
Some material adapted from Mohamed Younis, UMBC CMSC 611 Spr 2003 course slides
Some material adapted from Hennessy & Patterson / © 2003 Elsevier Science

## Slide 2: Sequential Laundry
Washer takes 30 min, Dryer takes 40 min, folding takes 20 min
Sequential laundry takes 6 hours for 4 loads
If they learned pipelining, how long would laundry take?
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
Slide: Dave Patterson
Time
A
B
C
D
T
a
s
k
O
r
d
e
r

## Slide 3: Pipelined Laundry
Pipelining means start work as soon as possible
Pipelined laundry takes 3.5 hours for 4 loads
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20
Slide: Dave Patterson

## Slide 4: Pipelining Lessons
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Pipeline rate limited by slowest pipeline stage
Multiple tasks operating simultaneously using different resources
Potential speedup = Number pipe stages
Unbalanced lengths of pipe stages reduces speedup
Time to “fill” pipeline and time to “drain” it reduce speedup
Stall for Dependencies
Time
6 PM
7
8
9
Slide: Dave Patterson
A
B
C
D
T
a
s
k
O
r
d
e
r
30
40
40
40
40
20

## Slide 5: MIPS Instruction Set
op
target address
0
26
31
6 bits
26 bits
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
RISC characterized by the following features that simplify implementation:
  All ALU operations apply only on registers
  Memory is affected only by load and store
  Instructions follow very few formats and typically are of the same size

## Slide 6: Single-cycle Execution
Figure: Dave Patterson

## Slide 7: Multi-Cycle Implementation of MIPS
Instruction fetch cycle (IF)
IR  Mem[PC]; NPC  PC + 4
Instruction decode/register fetch cycle (ID)
A  Regs[IR6..10]; B  Regs[IR11..15]; Imm  ((IR16)16 ##IR16..31)
Execution/effective address cycle (EX)
Memory ref: ALUOutput  A + Imm;
  Reg-Reg ALU: ALUOutput  A func B;
  Reg-Imm ALU: ALUOutput  A op Imm;
  Branch: ALUOutput  NPC + Imm; Cond  (A op 0)
Memory access/branch completion cycle (MEM)
  Memory ref: LMD  Mem[ALUOutput] or Mem(ALUOutput]  B;
  Branch: if (cond) PC ALUOutput;
Write-back cycle (WB)
  Reg-Reg ALU: Regs[IR16..20]  ALUOutput;
  Reg-Imm ALU: Regs[IR11..15]  ALUOutput;
  Load: Regs[IR11..15]  LMD;

## Slide 8: Multi-cycle Execution
Figure: Dave Patterson

## Slide 9: Stages of Instruction Execution
The load instruction is the longest
All instructions follows at most the following five steps:
  Ifetch: Instruction Fetch
    Fetch the instruction from the Instruction Memory and update PC
  Reg/Dec: Registers Fetch and Instruction Decode
  Exec: Calculate the memory address
  Mem: Read the data from the Data Memory
  WB: Write the data back to the register file
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Ifetch
Reg/Dec
Exec
Mem
WB
Load
Slide: Dave Patterson
Notes: As shown here, each of these five steps will take one clock cycle to complete.
And in pipeline terminology, each step is referred to as one stage of the pipeline.
+1 = 8 min. (X:48)

## Slide 10: Instruction Pipelining
IFetch
Dec
Exec
Mem
WB
IFetch
Dec
Exec
Mem
WB
IFetch
Dec
Exec
Mem
WB
IFetch
Dec
Exec
Mem
WB
IFetch
Dec
Exec
Mem
WB
IFetch
Dec
Exec
Mem
WB
Program Flow
Time
Pipelining improves performance by increasing instruction throughput
Start handling next instruction while the current instruction is in progress
Feasible when different devices at different stages

## Slide 11: Example of Instruction Pipelining
Ideal and upper bound for speedup is number of stages in the pipeline
Time between first & fourth instructions is 3  2 = 6 ns
Time between first & fourth instructions is 3  8 = 24 ns

## Slide 12: Single Cycle
Clk
Load
Store
Waste
Cycle 1
Cycle 2
Figure: Dave Patterson
Cycle time long enough for longest instruction
Shorter instructions waste time
No overlap
Notes: Here are the timing diagrams showing the differences between the single cycle, multiple cycle, and pipeline implementations.
For example, in the pipeline implementation, we can finish executing the Load, Store, and R-type instruction sequence in seven cycles.
In the multiple clock cycle implementation, however, we cannot start executing the store until Cycle 6 because we must wait for the load instruction to complete.
Similarly, we cannot start the execution of the R-type instruction until the store instruction has completed its execution in Cycle 9.
In the Single Cycle implementation, the cycle time is set to accommodate the longest instruction, the Load instruction.
Consequently, the cycle time for the Single Cycle implementation can be five times longer than the multiple cycle implementation.
But may be more importantly, since the cycle time has to be long enough for the load instruction, it is too long for the store instruction so the last part of the cycle here is wasted.
+2 = 77 min. (X:57)

## Slide 13: Multiple Cycle
Figure: Dave Patterson
Cycle time long enough for longest stage
Shorter stages waste time
Shorter instructions can take fewer cycles
No overlap
Cycle 1
Ifetch
Reg
Exec
Mem
Wr
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
Ifetch
Reg
Exec
Mem
Load
Store
Ifetch
R-type
Clk
Notes: Here are the timing diagrams showing the differences between the single cycle, multiple cycle, and pipeline implementations.
For example, in the pipeline implementation, we can finish executing the Load, Store, and R-type instruction sequence in seven cycles.
In the multiple clock cycle implementation, however, we cannot start executing the store until Cycle 6 because we must wait for the load instruction to complete.
Similarly, we cannot start the execution of the R-type instruction until the store instruction has completed its execution in Cycle 9.
In the Single Cycle implementation, the cycle time is set to accommodate the longest instruction, the Load instruction.
Consequently, the cycle time for the Single Cycle implementation can be five times longer than the multiple cycle implementation.
But may be more importantly, since the cycle time has to be long enough for the load instruction, it is too long for the store instruction so the last part of the cycle here is wasted.
+2 = 77 min. (X:57)

## Slide 14: Pipeline
Figure: Dave Patterson
Cycle time long enough for longest stage
Shorter stages waste time
No additional benefit from shorter instructions
Overlap instruction execution
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
Clk
Load
Ifetch
Reg
Exec
Mem
Wr
Ifetch
Reg
Exec
Mem
Wr
Store
Ifetch
Reg
Exec
Mem
Wr
R-type
Notes: Here are the timing diagrams showing the differences between the single cycle, multiple cycle, and pipeline implementations.
For example, in the pipeline implementation, we can finish executing the Load, Store, and R-type instruction sequence in seven cycles.
In the multiple clock cycle implementation, however, we cannot start executing the store until Cycle 6 because we must wait for the load instruction to complete.
Similarly, we cannot start the execution of the R-type instruction until the store instruction has completed its execution in Cycle 9.
In the Single Cycle implementation, the cycle time is set to accommodate the longest instruction, the Load instruction.
Consequently, the cycle time for the Single Cycle implementation can be five times longer than the multiple cycle implementation.
But may be more importantly, since the cycle time has to be long enough for the load instruction, it is too long for the store instruction so the last part of the cycle here is wasted.
+2 = 77 min. (X:57)

## Slide 15: Pipeline Performance
Pipeline increases the instruction throughput
  not execution time of an individual instruction
An individual instruction can be slower:
  Additional pipeline control
  Imbalance among pipeline stages
Suppose we execute 100 instructions:
  Single Cycle Machine
    45 ns/cycle x 1 CPI x 100 inst = 4500 ns
  Multi-cycle Machine
    10 ns/cycle x 4.2 CPI (due to inst mix) x 100 inst = 4200 ns
  Ideal 5 stages pipelined machine
    10 ns/cycle x (1 CPI x 100 inst + 4 cycle drain) = 1040 ns
Lose performance due to fill and drain

## Slide 16: Pipeline Datapath
Data Stationary
Every stage must be completed in one clock cycle to avoid stalls
Values must be latched to ensure correct execution of instructions
The PC multiplexer has moved to the IF stage to prevent two instructions from updating the PC simultaneously (in case of branch instruction)

## Slide 17: Pipeline Stage Interface

## Slide 18: Pipeline Hazards
Cases that affect instruction execution semantics and thus need to be detected and corrected
Hazards types
  Structural hazard: attempt to use a resource two different ways at same time
    Single memory for instruction and data
  Data hazard: attempt to use item before it is ready
    Instruction depends on result of prior instruction still in the pipeline
  Control hazard: attempt to make a decision before condition is evaluated
    branch instructions
Hazards can always be resolved by waiting

## Slide 19: Visualizing Pipelining
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Slide: David Culler

## Slide 20: Example: One Memory Port/Structural Hazard
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Instr 3
Instr 4
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
DMem
Structural Hazard
Slide: David Culler

## Slide 21: Resolving Structural Hazards
Wait
  Must detect the hazard
    Easier with uniform ISA
  Must have mechanism to stall
    Easier with uniform pipeline organization
Throw more hardware at the problem
  Use instruction & data cache rather than direct access to memory

## Slide 22: Detecting and Resolving Structural Hazard
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Stall
Instr 3
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg
Bubble
Bubble
Bubble
Bubble
Bubble
Slide: David Culler

## Slide 23: Stalls & Pipeline Performance
Assuming all pipeline stages are balanced

## Slide 24: Data Hazards
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Time (clock cycles)
IF
ID/RF
EX
MEM
WB
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Slide: David Culler
Reg
ALU
DMem
Ifetch
Reg

## Slide 25: Three Generic Data Hazards
I: add r1,r2,r3
J: sub r4,r1,r3
Read After Write (RAW) InstrJ tries to read operand before InstrI writes it
Caused by a “Data Dependence” (in compiler nomenclature). This hazard results from an actual need for communication.
Slide: David Culler

## Slide 26: Three Generic Data Hazards
Write After Read (WAR) InstrJ writes operand before InstrI reads it
Called an “anti-dependence” in compilers.
  This results from reuse of the name “r1”.
Can’t happen in MIPS 5 stage pipeline because:
  All instructions take 5 stages, and
  Reads are always in stage 2, and
  Writes are always in stage 5
I: sub r4,r1,r3
J: add r1,r2,r3
K: mul r6,r1,r7
Slide: David Culler

## Slide 27: Three Generic Data Hazards
Write After Write (WAW) InstrJ writes operand before InstrI writes it.
Called an “output dependence” in compilers
  This also results from the reuse of name “r1”.
Can’t happen in MIPS 5 stage pipeline:
  All instructions take 5 stages, and
  Writes are always in stage 5
Do see WAR and WAW in more complicated pipes
I: mul r1,r4,r3
J: add r1,r2,r3
K: sub r6,r1,r7
Slide: David Culler

## Slide 28: Forwarding to Avoid Data Hazard
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Slide: David Culler

## Slide 29: HW Change for Forwarding
MEM/WR
ID/EX
EX/MEM
Data
Memory
ALU
mux
mux
Registers
NextPC
Immediate
mux
Slide: David Culler

## Slide 30: Data Hazard Even with Forwarding
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
or r8,r1,r9
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Slide: David Culler
Notes: MIPS actutally didn’t interlecok: MPU without Interlocked Pipelined Stages

## Slide 31: Resolving Load Hazards
Adding hardware? How? Where?
Detection?
Compilation techniques?
What is the cost of load delays?
Slide: David Culler

## Slide 32: Resolving the Load Data Hazard
Time (clock cycles)
or r8,r1,r9
I
n
s
t
r.
O
r
d
e
r
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
Reg
ALU
DMem
Ifetch
Reg
Ifetch
ALU
DMem
Bubble
Reg
Reg
Ifetch
ALU
DMem
Reg
Bubble
Ifetch
ALU
DMem
Reg
Bubble
Reg
How is this different from the instruction issue stall?
Slide: David Culler

## Slide 33: Software Scheduling to Avoid Load Hazards
Try producing fast code for
a = b + c;
d = e – f;
assuming a, b, c, d ,e, and f in memory.
Slow code:
LW Rb,b
LW Rc,c
ADD Ra,Rb,Rc
SW a,Ra
LW Re,e
LW Rf,f
SUB Rd,Re,Rf
SW d,Rd
Fast code:
LW Rb,b
LW Rc,c
LW Re,e
ADD Ra,Rb,Rc
LW Rf,f
SW a,Ra
SUB Rd,Re,Rf
SW d,Rd
Slide: David Culler

## Slide 34: Instruction Set Connection
What is exposed about this organizational hazard in the instruction set?
k cycle delay?
  bad, CPI is not part of ISA
k instruction slot delay
  load should not be followed by use of the value in the next k instructions
Nothing, but code can reduce run-time delays
MIPS did the transformation in the assembler
Slide: David Culler

## Slide 35: Pipeline Hazards
Cases that affect instruction execution semantics and thus need to be detected and corrected
Hazards types
  Structural hazard: attempt to use a resource two different ways at same time
    Single memory for instruction and data
  Data hazard: attempt to use item before it is ready
    Instruction depends on result of prior instruction still in the pipeline
  Control hazard: attempt to make a decision before condition is evaluated
    branch instructions
Hazards can always be resolved by waiting

## Slide 36: Control Hazard on Branches Three Stage Stall
10: beq r1,r3,36
14: and r2,r3,r5
18: or r6,r1,r7
22: add r8,r1,r9
36: xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Slide: David Culler

## Slide 37: Example: Branch Stall Impact
If 30% branch, 3-cycle stall significant!
Two part solution:
  Determine branch taken or not sooner, AND
  Compute taken branch address earlier
MIPS branch tests if register = 0 or  0
MIPS Solution:
  Move Zero test to ID/RF stage
  Adder to calculate new PC in ID/RF stage
  1 clock cycle penalty for branch versus 3
Slide: David Culler

## Slide 38: Pipelined MIPS Datapath
Add
Zero?
Figure: Dave Patterson

## Slide 39: Four Branch Hazard Alternatives
Stall until branch direction is clear
Predict Branch Not Taken
  Execute successor instructions in sequence
  “Squash” instructions in pipeline if branch taken
  Advantage of late pipeline state update
  47% MIPS branches not taken on average
  PC+4 already calculated, so use it to get next instruction
Predict Branch Taken
  53% MIPS branches taken on average
  But haven’t calculated branch target address in MIPS
    MIPS still incurs 1 cycle branch penalty
    Other machines: branch target known before outcome
Slide: David Culler

## Slide 40: Four Branch Hazard Alternatives
Delayed Branch
  Define branch to take place AFTER a following instruction branch instruction sequential successor1 sequential successor2 ........ sequential successorn ........
  branch target if taken
  1 slot delay allows proper decision and branch target address in 5 stage pipeline
  MIPS uses this
Branch delay of length n
Slide: David Culler

## Slide 41: Delayed Branch
Where to get branch delay slot instructions?
  Before branch instruction
  From the target address
    only valuable when branch taken
  From fall through
    only valuable when branch not taken
  Canceling branches allow more slots to be filled
Compiler effectiveness for single delay slot:
  Fills about 60% of branch delay slots
  About 80% of instructions executed in branch delay slots useful in computation
  48% (60% x 80%) of slots usefully filled
Delayed Branch downside: 7-8 stage pipelines, multiple instructions issued per clock (superscalar)
Slide: David Culler

## Slide 42: Scheduling Branch-Delay Slots
Best scenario
Good for loops
Good taken strategy
R4 must be temp reg.

## Slide 43: Branch-Delay Scheduling Requirements
Limitation on delayed-branch scheduling arise from:
  Restrictions on instructions scheduled into the delay slots
  Ability to predict at compile-time whether a branch is likely to be taken
May have to fill with a no-op instruction
  Average 30% wasted
Additional PC is needed to allow safe operation in case of interrupts (more on this later)

## Slide 44: Example: Evaluating Branch Alternatives
Assume:
14% Conditional & Unconditional
65% Taken; 52% Delay slots not usefully filled
Scheduling Scheme | Branch Penalty | CPI | Pipeline Speedup | Speedup vs stall
Stall pipeline | 3.00 | 1.42 | 3.52 | 1.00
Predict taken | 1.00 | 1.14 | 4.39 | 1.25
Predict not taken | 1.00 | 1.09 | 4.58 | 1.30
Delayed branch | 0.52 | 1.07 | 4.66 | 1.32
Slide: David Culler
Notes: Stall: 1+.14(branches)*3(cycle stall)
Taken: 1+.14(branches)*(.65(taken)*1(delay to find address)+.35(not taken)*1(penalty))
Not taken: 1+.14*(.65(taken)*1+[.35(not taken)*0])
Delayed: 1+.14*(.52(not usefully filled)*1)