## Slide 1: Some Intel CPU examples
Figures and data from Arstechnica
arstechnica.com/old/content/2004/07/pentium-1.ars
arstechnica.com/old/content/2001/05/p4andg4e.ars
arstechnica.com/old/content/2004/02/pentium-m.ars
arstechnica.com/hardware/news/2006/04/core.ars
arstechnica.com/hardware/news/2008/04/what-you-need-to-know-about-nehalem.ars

## Slide 2: Pentium
Notes: Dual issue
2 5-stage integer pipes (some restrictions & coupling)
  1: Prefetch/fetch – align in prefetch buffer for decoding (variable instruction size)
  2: Decode 1 – decode to internal format, branch prediction
  3: Decode 2 – complex decode, address computation
  4: Execute
  5: Write Back
1 6-stage float pipe
Branch prediction ~75%

## Slide 3: Pentium Pro, II, III
Notes: 3 instruction issue (2 simple/fast, 1 complex)
ROB = 40-entry rotating queue, visited twice
  Rename in ROB to 40 microarchitectural registers
RS up to 20 instructions
Execution
  5 issue ports
  Store addr & store data
  1 cycle for most, *,/ 4-cycle latency, 1-cycle issue
12-stage pipeline
  1-4.5: BTB & Instruction fetch
  4.5-6: Decode
  7: register rename/ROB
  8: write to RS
  9: issue
  10: execute
  11-12: retire
Branch prediction
  90+%

## Slide 4: P4 (Pentium 4)
Notes: Trace cache: decoded instruction blocks (90% hit rate)
  ROM for long instructions
  Mini BTB for trace cache branches
20+ stage pipeline
  More on cache miss (10?)
  1-2: Trace cache next IP
  3-4: Trace cache fetch
  5: Drive signals across chip
  6-8: Allocate & rename (128 microarchitectural registers)
  9: Queue
  10-12: Schedule
  13-14: Dispatch (up to 6 per cycle)
  15-16: Register file
  17: Execute
  18: Flags
  19: Branch check
  20: Drive signals across chip

## Slide 5: Pentium M
Notes: Branch Prediction
  4k BTB
  Loop predictor + “indirect” predictor
Micro op fusion to avoid ROB

## Slide 6: Core
Notes: 96-entry ROB

## Slide 7: Core Decode
Notes: 4-7 (w/ fusion) issue to 7 micro op
  More x86 into single micro-ops
  Macro-fusion to merge across x86 ops
  Micro-op fusion to avoid ROB
Branch prediction
  Loop predictor
  Indirect predictor / BTB
    Target address by condition

## Slide 8: Memory Speculation
Notes: Cannot rearrange load/store for fear of aliasing
Assume no aliasing, restart if wrong

## Slide 9: Nehalem
Notes: Decode
  Loop
Execute
  Rely on simultaneous multithreading / hyperthreading
  128-entry ROB (partitioned by thread)
  36-entry RS