## Slide 1: CMSC 611: Advanced Computer Architecture
I/O & Storage
Some material adapted from Mohamed Younis, UMBC CMSC 611 Spr 2003 course slides
Some material adapted from Hennessy & Patterson / © 2003 Elsevier Science

## Slide 2: Input/Output
I/O Interface
  Device drivers
  Device controller
  Service queues
  Interrupt handling
Design Issues
  Performance
  Expandability
  Standardization
  Resilience to failure
Impact on Tasks
  Blocking conditions
  Priority inversion
  Access ordering
Processor
Computer
Control
Datapath
Memory
Devices
Input
Output
Processor
Computer
Control
Datapath
Memory
Devices
Input
Output
Network

## Slide 3: Impact of I/O on System Performance
Suppose we have a benchmark that executes in 100 seconds of elapsed time, where 90 seconds is CPU time and the rest is I/O time. If the CPU time improves by 50% per year for the next five years but I/O time does not improve, how much faster will our program run at the end of the five years?
Answer: Elapsed Time = CPU time + I/O time
Over five years:
CPU improvement = 90/12 = 7. BUT System improvement = 100/22 = 4.5

## Slide 4: Typical I/O System
Processor
Cache
Memory - I/O Bus
Main
Memory
I/O
Controller
Disk
Disk
I/O
Controller
I/O
Controller
Graphics
Network
interrupts
The connection between the I/O devices, processor, and memory are usually called (local or internal) bus
Communication among the devices and the processor use both protocols on the bus and interrupts

## Slide 5: I/O Device Examples
Device Behavior Partner Data Rate (KB/sec)
Keyboard Input Human 0.01
Mouse Input Human 0.02
Line Printer Output Human 1.00
Floppy disk Storage Machine 50.00
Laser Printer Output Human 100.00
Optical Disk Storage Machine 500.00
Magnetic Disk Storage Machine 5,000.00
Network-LAN Input or Output Machine 20 – 1,000.00
Graphics Display Output Human 30,000.00
Notes: Here are some examples of the various I/O devices you are probably familiar with.
Notice that most I/O devices that has human as their partner usually has relatively low peak data rates because human in general are slow relatively to the computer system.
The exceptions are the laser printer and the graphic displays.
Laser printer requires a high data rate because it takes a lot of bits to describe high resolution image you like to print by the laser writer.
The graphic display requires a high data rate because as I will show you later in today’s lecture, all the color objects we see in the real world and taken for granted is very hard to replicate on a graphic display.
Let’s take a closer look at one of the most popular storage device, magnetic disks.
+2 = 28 min. (Y:08)

## Slide 6: Disk History
Data density in
Mbit/square inch
Capacity of Unit Shown in Megabytes
source: New York Times, 2/23/98, page C3

## Slide 7: Organization of a Hard Magnetic Disk
Typical numbers (depending on the disk size):
  500 to 2,000 tracks per surface
  32 to 128 sectors per track
    A sector is the smallest unit that can be read or written to
Traditionally all tracks have the same number of sectors:
  Constant bit density: record more sectors on the outer tracks
  Recently relaxed: constant bit size, speed varies with track location
Platters
Track
Sector
Notes: Here is a primitive picture showing you how a disk drive can have multiple platters.
Each surface on the platter are divided into tracks and each track is further divided into sectors. A sector is the smallest unit that can be read or written.
By simple geometry you know the outer track have more area and you would thing the outer tack will have more sectors.
This, however, is not the case in traditional disk design where all tracks have the same number of sectors. Well, you will say, this is dumb but dumb is the reason they do it .
By keeping the number of sectors the same, the disk controller hardware and software can be dumb and does not have to know which track has how many sectors.
With more intelligent disk controller hardware and software, it is getting more popular to record more sectors on the outer tracks. This is referred to as constant bit density.
+2 = 32 min. (Y:12)

## Slide 8: Magnetic Disk Operation
Cylinder
Sector
Track
Head
Platter
Cylinder: all the tracks under the head at a given point on all surface
Read/write is a three-stage process:
  Seek time
    position the arm over proper track
  Rotational latency
    wait for the sector to rotate under the read/write head
  Transfer time
    transfer a block of bits (sector) under the read-write head
Average seek time
  (∑ time for all possible seeks) / (# seeks)
  Typically in the range of 8 ms to 12 ms
  Due to locality of disk reference, actual average seek time may only be 25% to 33% of the advertised number
Notes: To read write information into a sector, a movable arm containing a read/write head is located over each surface.
The term cylinder is used to refer to all the tracks under the read/write head at a given point on all surfaces.
To access data, the operating system must direct the disk through a 3-stage process.
(a) The first step is to position the arm over the proper track. This is the seek operation and the time to complete this operation is called the seek time.
(b) Once the head has reached the correct track, we must wait for the desired sector to rotate under the read/write head. This is referred to as the rotational latency.
(c) Finally, once the desired sector is under the read/write head, the data transfer can begin.
The average seek time as reported by the manufacturer is in the range of 12 ms to 20ms and is calculated as the sum of the time for all possible seeks divided by the number of possible seeks.
This number is usually on the pessimistic side because due to locality of disk reference, the actual average seek time may only be 25 to 33% of the number published.
+2 = 34 min. (Y:14)

## Slide 9: Magnetic Disk Characteristic
Rotational Latency:
  Most disks rotate at 5,400 to 10,000 RPM
  Approximately 11 ms to 6 ms per revolution, respectively
  An average latency to the desired information is halfway around the disk:
    5.5 ms at 5400 RPM, 3 ms at 10000 RPM
Transfer Time is a function of :
  Transfer size (usually a sector): 1 KB / sector
  Rotation speed: 5400 RPM to 10000 RPM
  Recording density: bits per inch on a track
  Diameter: typical diameter ranges from 2.5 to 5.25”
  Typical values ~500MB per second
Notes: As far as rotational latency is concerned, most disks rotate at 3,600 RPM or approximately 16 ms per revolution.
Since on average, the information you desired is half way around the disk, the average rotational latency will be 8ms.
The transfer time is a function of transfer size, rotation speed, and recording density.
The typical transfer speed is 2 to 4 MB per second.
Notice that the transfer time is much faster than the rotational latency and seek time.
This is similar to the DRAM situation where the DRAM access time is much shorter than the DRAM cycle time.
***** Do anybody remember what we did to take advantage of the short access time versus cycle time? Well, we interleave!
+2 = 36 min. (Y:16)

## Slide 10: Example
Calculate the access time for a disk with 512 byte/sector and 12 ms advertised seek time. The disk rotates at 5400 RPM and transfers data at a rate of 4MB/sec. The controller overhead is 1 ms. Assume that the queue is idle (so no service time)
Answer:
Disk Access Time = Seek time + Rotational Latency + Transfer time
  + Controller Time + Queuing Delay
= 12 ms + 0.5 / 5400 RPM + 0.5 KB / 4 MB/s + 1 ms + 0
= 12 ms + 0.5 / 90 RPS + 0.125 / 1024 s + 1 ms + 0
= 12 ms + 5.5 ms + 0.1 ms + 1 ms + 0 ms
= 18.6 ms
If real seeks are 1/3 the advertised seeks, disk access time would be
10.6 ms, with rotation delay contributing 50% of the access time!

## Slide 11: Historical Trend
Characteristics IBM 3090 IBM UltraStar Integral 1820
Disk diameter (inches) 10.88 3.50 1.80
Formatted data capacity (MB) 22,700 4,300 21
MTTF (hours) 50,000 1,000,000 100,000
Number of arms/box 12 1 1
Rotation speed (RPM) 3,600 7,200 3,800
Transfer rate (MB/sec) 4.2 9-12 1.9
Power/box (watts) 2,900 13 2
MB/watt 8 102 10.5
Volume (cubic feet) 97 0.13 0.02
MB/cubic feet 234 33000 1050
Notes: Here are some examples of the disks you can buy.
Large diameter drives have more mega bytes to amortize the cost of electronics so the traditional wisdom was that they had the lowest cost per megabyte.
But this advantage is offset when the small drives are used by PC which has much much higher sales volume to drive down the cost.
Also, as you can see here, the small disk drives (right most column) also have the advantages in power (2 vs 2900) and volume (0.02 versus 97).
You probably don’t want one of these (2.9 Kilo Watt) in your house unless you live in Alaska and don’t have a heater in the winter.
The MTTF is the mean time to failure which is a common measure of reliability.
+2 = 42 min. (Y:22)

## Slide 12: Reliability and Availability
Two terms that are often confused:
  Reliability: Is anything broken?
  Availability: Is the system still available to the user?
Availability can be improved by adding hardware:
  Example: adding ECC on memory
Reliability can only be improved by:
  Enhancing environmental conditions
  Building more reliable components
  Building with fewer components
    Improve availability may come at the cost of lower reliability
Notes: This bring us to two terms that are often confused: reliability and availability.
Here is the proper distinction: reliability asks the question is anything broken?
Availability, on the other hand, ask the question is the system still availability to the user?
Adding hardware can therefore improve availability. For example, an airplane with two engines is more “available” than an airplane with one engine.
Reliability, on the other hand, can only be improved by bettering environmental conditions, building more reliable components, or reduce the number of components in the system.
Notice that by adding hardware to improve availability, you may actually reduce reliability.
For example, an airplane with two engines is twice as likely to have an engine failure than an airplane with only one engine so its reliability is lower although its availability is higher.
+2 = 44 min. (Y:24)

## Slide 13: Disk Arrays
Increase potential throughput by having many disk drives:
  Data is spread over multiple disk
  Multiple accesses are made to several disks
Reliability is lower than a single disk:
  Reliability of N disks = Reliability of 1 Disk ÷ N
    (50,000 Hours ÷ 70 disks = 700 hours)
    Disk system MTTF: Drops from 6 years to 1 month
  Arrays (without redundancy) too unreliable to be useful!
  But availability can be improved by adding redundant disks (RAID):
    Lost information can be reconstructed from redundant information
Notes: The discussion of reliability and availability brings us to a new organization of disk storage where arrays of small and inexpensive disks are used to increase the potential throughput.
This is how it works: Data is spread over multiple disk so multiple accesses can be made to several disks either via interleaving or done in parallel.
While disk arrays improve throughput, latency is not necessary improved.
Also with N disks in the disk array, its reliability is only 1 over N the reliability of a single disk.
But availability can be improved by adding redundant disks so lost information can be reconstructed from redundant information.
Since mean time to repair is measured in hours and MTTF is measured in years, redundancy can make the availability of disk arrays much higher than that of a single disk.
+2 = 46 min. (Y:26)

## Slide 14: Manufacturing Advantages of Disk Arrays
14”
10”
5.25”
3.5”
3.5”
Disk Array: 1 disk design
Conventional: 4 disk designs
Low End
High End
Disk Product Families
Replace Small # of Large Disks with Large # of Small Disks!

## Slide 15: Redundant Arrays of Disks
Redundant Array of Inexpensive Disks (RIAD)
  Widely available and used in today’s market
  Files are "striped" across multiple spindles
  Redundancy yields high data availability despite low reliability
  Contents of a failed disk is reconstructed from data redundantly stored in the disk array
  Drawbacks include capacity penalty to store redundant data and bandwidth penalty to update a disk block
  Different levels based on replication level and recovery techniques

## Slide 16: RAID 1: Disk Mirroring/Shadowing
Targeted for high I/O rate , high availability environments
recovery
group
Each disk is fully duplicated onto its "shadow“
Very high availability can be achieved
Bandwidth sacrifice on write: Logical write = two physical writes
Reads may be optimized
Most expensive solution: 100% capacity overhead

## Slide 17: RAID 3: Parity Disk
P
10010011
11001101
10010011
. . .
logical record
1
0
0
1
0
0
1
1
1
1
0
0
1
1
0
1
1
0
0
1
0
0
1
1
0
0
1
1
0
0
0
0
Striped physical
records
Parity computed across recovery group to protect against hard disk failures
33% capacity cost for parity in this configuration: wider arrays reduce
capacity costs, decrease expected availability, increase reconstruction time
Arms logically synchronized, spindles rotationally synchronized
(logically a single high capacity, high transfer rate disk)
Targeted for high bandwidth applications: Scientific, Image Processing

## Slide 18
Block-Based Parity
Block-based parity leads to more efficient read access compared to RAID 3
Designating a parity disk allows recovery but will keep it idle in the absence
of a disk failure
RAID 5 distribute the parity block to allow the use of all disk and enhance
parallelism of disk access
RAID 4
RAID 5

## Slide 19: RAID 5+: High I/O Rate Parity
A logical write
becomes four
physical I/Os
Independent writes
possible because of
interleaved parity
Reed-Solomon
Codes ("Q") for
protection during
reconstruction
D0
D1
D2
D3
P
D4
D5
D6
P
D7
D8
D9
P
D10
D11
D12
P
D13
D14
D15
P
D16
D17
D18
D19
D20
D21
D22
D23
P
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
Disk Columns
Increasing
Logical
Disk
Addresses
Stripe
Stripe
Unit
Targeted for mixed
applications

## Slide 20: Problems of Small Writes
D0
D1
D2
D3
P
D0'
+
+
D0'
D1
D2
D3
P'
new
data
old
data
old
parity
XOR
XOR
(1. Read)
(2. Read)
(3. Write)
(4. Write)
RAID-5: Small Write Algorithm
1 Logical Write = 2 Physical Reads + 2 Physical Writes

## Slide 21: Subsystem Organization
host
array
controller
single board
disk
controller
single board
disk
controller
single board
disk
controller
single board
disk
controller
host
adapter
manages interface
to host, DMA
control, buffering,
parity logic
physical device
control
often piggy-backed
in small format devices
striping software off-loaded from
host to array controller
no applications modifications
no reduction of host performance

## Slide 22: System Availability: Orthogonal RAIDs
Array
Controller
String
Controller
String
Controller
String
Controller
String
Controller
String
Controller
String
Controller
. . .
. . .
. . .
. . .
. . .
. . .
Data Recovery Group: unit of data redundancy
Redundant Support Components: fans, power supplies, controller, cables
End to End Data Integrity: internal parity protected data paths

## Slide 23: I/O Control
Processor
Cache
Memory - I/O Bus
Main
Memory
I/O
Controller
Disk
Disk
I/O
Controller
I/O
Controller
Graphics
Network
interrupts

## Slide 24: Polling: Programmed I/O
Advantage:
  Simple: the processor is totally in control and does all the work
Disadvantage:
  Polling overhead can consume a lot of CPU time
CPU
IOC
device
Memory
Is the
data
ready?
read
data
store
data
yes
no
done?
no
yes
busy wait loop
not an efficient
way to use the CPU
unless the device
is very fast!
but checks for I/O
completion can be
dispersed among
computation
intensive code
Notes: In Polling, the I/O device put information in a status register and the OS periodically check it (the busy loop) to see if the data is ready or if an error condition has occurred.
If the data is ready, fine: read the data and move on. If not, we stay in this loop and try again at a later time.
The advantage of this approach is simple: the processor is totally in control and does all the work but the processor in total control is also the problem.
Needless to say, polling overhead can consume a lot of CPU time if the device is very fast.
For this reason (Disadvantage), most I/O devices notify the processor via I/O interrupt.
+2 = 60 min. (Y:40)

## Slide 25: Interrupt Driven Data Transfer
Advantage:
  User program progress is only halted during actual transfer
Disadvantage: special hardware is needed to:
  Cause an interrupt (I/O device)
  Detect an interrupt (processor)
  Save the proper states to resume after the interrupt (processor)
add
sub
and
or
nop
read
store
...
rti
memory
user
program
(1) I/O
interrupt
(2) save PC
(3) interrupt
service addr
interrupt
service
routine
(4)
CPU
IOC
device
Memory
:
Notes: That is, whenever an I/O device needs attention from the processor, it interrupts the processor from what it is currently doing.
This is how an I/O interrupt looks in the overall scheme of things. The processor is minding its business when one of the I/O device wants its attention and causes an I/O interrupt.
The processor then save the current PC, branch to the address where the interrupt service routine resides, and start executing the interrupt service routine.
When it finishes executing the interrupt service routine, it branches back to the point of the original program where we stop and continue.
The advantage of this approach is efficiency. The user program’s progress is halted only during actual transfer.
The disadvantage is that it require special hardware in the I/O device to generate the interrupt. And on the processor side, we need special hardware to detect the interrupt and then to save the proper states so we can resume after the interrupt.
+2 = 62 min. (Y:42)

## Slide 26: I/O Interrupt vs. Exception
An I/O interrupt is just like the exceptions except:
  An I/O interrupt is asynchronous
  Further information needs to be conveyed
  Typically exceptions are more urgent than interrupts
An I/O interrupt is asynchronous with respect to instruction execution:
  I/O interrupt is not associated with any instruction
  I/O interrupt does not prevent any instruction from completion
    You can pick your own convenient point to take an interrupt
I/O interrupt is more complicated than exception:
  Needs to convey the identity of the device generating the interrupt
  Interrupt requests can have different urgencies:
    Interrupt request needs to be prioritized
    Priority indicates urgency of dealing with the interrupt
    high speed devices usually receive highest priority
Notes: How does an I/O interrupt different from the exception you already learned?
Well, an I/O interrupt is asynchronous with respect to the instruction execution while exception such as overflow or page fault are always associated with a certain instruction.
Also for exception, the only information needs to be conveyed is the fact that an exceptional condition has occurred but for interrupt, there is more information to be conveyed.
Let me elaborate on each of these two points.
Unlike exception, which is always associated with an instruction, interrupt is not associated with any instruction. The user program is just doing its things when an I/O interrupt occurs.
So I/O interrupt does not prevent any instruction from completing so you can pick your own convenient point to take the interrupt.
As far as conveying more information is concerned, the interrupt detection hardware must somehow let the OS know who is causing the interrupt.
Furthermore, interrupt requests needs to be prioritized. The hardware that can do all these looks like this.
+2 = 64 min. (Y:44)

## Slide 27: Direct Memory Access
Direct Memory Access (DMA):
  External to the CPU
  Use idle bus cycles (cycle stealing)
  Act as a master on the bus
  Transfer blocks of data to or from memory without CPU intervention
  Efficient for large data transfer, e.g. from disk
  Cache usage allows the processor to leave enough memory bandwidth for DMA
CPU
IOC
device
Memory
DMAC
CPU sends a starting address,
direction, and length count
to DMAC. Then issues "start".
DMAC provides handshake
signals for Peripheral
Controller, and Memory
Addresses and handshake
signals for Memory.
How does DMA work?:
  CPU sets up and supply device id, memory address, number of bytes
  DMA controller (DMAC) starts the access and becomes bus master
  For multiple byte transfer, the DMAC increment the address
  DMAC interrupts the CPU upon completion
For multiple bus system, each bus controller often contains DMA control logic
Notes: Finally, lets see how we can delegate some of the I/O responsibilities from the CPU.
The first option is Direct Memory Access which take advantage of the fact that I/O events often involve block transfer: you are not going to access the disk 1 byte at a time.
The DMA controller is external to the processor and can acts as a bus master to transfer blocks of data to or from memory and the I/O device without CPU intervention.
This is how it works. The CPU sends the starting address, the direction and length of the transfer to the DMA controller and issues a start command.
The DMA controller then take over from there and provides handshake signals required (point to the last text block) to complete the entire block transfer.
So the DMA controller are pretty intelligent. If you add more intelligent to the DMA controller, you will end up with a IO processor or IOP for short.
+2 = 72 min. (Y:52)

## Slide 28
With virtual memory systems: (pages would have physical and virtual addresses)
  Physical pages re-mapping to different virtual pages during DMA operations
  Multi-page DMA cannot assume consecutive addresses
Solutions:
  Allow virtual addressing based DMA
    Add translation logic to DMA controller
    OS allocated virtual pages to DMA prevent re-mapping until DMA completes
  Partitioned DMA
    Break DMA transfer into multi-DMA operations, each is single page
    OS chains the pages for the requester
In cache-based systems: (there can be two copies of data items)
  Processor might not know that the cache and memory pages are different
  Write-back caches can overwrite I/O data or makes DMA to read wrong data
Solutions:
  Route I/O activities through the cache
    Not efficient since I/O data usually is not demonstrating temporal locality
  OS selectively invalidates cache blocks before I/O read or force write-back prior
  to I/O write
    Usually called cache flushing and requires hardware support
DMA Problems
DMA allows another path to main memory with no cache and address translation

## Slide 29: I/O Processor
CPU
IOP
Mem
D1
D2
Dn
. . .
main memory
bus
I/O
bus
CPU
IOP
(1) Issues
instruction
to IOP
memory
(2)
(3)
Device to/from memory
transfers are controlled
by the IOP directly.
IOP steals memory cycles.
OP Device Address
target device
where cmnds are
IOP looks in memory for commands
OP Addr Cnt Other
what
to do
where
to put
data
how
much
special
requests
(4) IOP interrupts
CPU when done
An I/O processor (IOP) offload the CPU
Some processors, e.g.
Motorola 860, include special purpose
IOP for serial communication
Notes: The IOP is so smart that the CPU only needs to issue a simple instruction (Op, Device, Address) that tells them what is the target device and where to find more commands (Addr).
The IOP will then fetch commands such as this (OP, Addr, Cnt, Other) from memory and do all the necessary data transfer between the I/O device and the memory system.
The IOP will do the transfer at the background and it will not affect the CPU because it will access the memory only when the CPU is not using it: this is called stealing memory cycles.
Only when the IOP finishes its operation will it interrupts the CPU.
+2 = 74 min. (Y:54)