## Slide 1: CMSC 611: Advanced Computer Architecture
Tomasulo
Some material adapted from Mohamed Younis, UMBC CMSC 611 Spr 2003 course slides
Some material adapted from Hennessy & Patterson / © 2003 Elsevier Science

## Slide 2: Scoreboard Summary
Why in HW at run time?
  Works when can’t know real dependence at compile time
  Compiler simpler
  Code for one machine runs well on another
Key idea: Allow instructions behind stall to proceed
  Enables out-of-order execution / out-of-order completion
  ID stage checked both for structural and data hazards
Out-of-order execution divides ID stage:
  Issue—decode instructions, check for structural hazards
  Read operands—wait until no data hazards, then read
CDC 6600
  Speedup 1.7 from compiler
  No forwarding (First write register then read it)
  Limited to instructions in basic block (small window)
  Number of functional units (structural hazards)
  Wait for WAR hazards

## Slide 3: Tomasulo’s Algorithm vs. Scoreboard
Tomasulo’s algorithm lead to Alpha 21264, HP 8000, MIPS 10000, Pentium II, PowerPC 604
Many differences from scoreboard
  Register renaming to avoid WAR and WAW
Control & buffers distributed with Function Units (FU) vs. centralized in scoreboard;
  FU buffers called “reservation stations”; have pending operands

## Slide 4: Tomasulo “Register Renaming”
Registers in instructions replaced by values or pointers to reservation stations(RS)
  avoids WAR, WAW hazards
  More reservation stations than registers
  Can do optimizations compilers cannot perform
Operands to FU from RS, not registers
Results broadcast over Common Data Bus
Load and Stores treated as FU w/ RS
Integer instructions can go past branches, allowing FP operations beyond basic block in FP queue

## Slide 5: Tomasulo Organization
The reservation stations hold instructions that had been issued and are awaiting execution at a functional unit
All results from FP FU and loads are broadcasted on the CDB
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 6: Reservation Station Components
Functional Unit Reservation Station
  Op—Operation to perform in the unit (e.g., + or –)
  Vj, Vk—Value of Source operands
    Store buffers has V field, result to be stored
  Qj, Qk—Reservation stations producing source registers (value to be written)
    Note: No ready flags as in Scoreboard; Qj,Qk=0 => ready
    Store buffers only have Qi for RS producing result
  Busy—Indicates reservation station or FU is busy
Register Reservation Station
  Register result status—Indicates which functional unit will write each register, if one exists. Blank when no pending instructions that will write that register.
Notes: What you might have thought
1. 4 stages of instruction executino
2.Status of FU: Normal things to keep track of (RAW & structura for busyl):
Fi from instruction format of the mahine (Fi is dest)
Add unit can Add or Sub
Rj, Rk - status of registers (Yes means ready)
Qj,Qk - If a no in Rj, Rk, means waiting for a FU to write result; Qj, Qk means wihch FU waiting for it
3.Status of register result (WAW &WAR)s:
which FU is going to write into registers
Scoreboard on 6600 = size of FU
6.7, 6.8, 6.9, 6.12, 6.13, 6.16, 6.17
FU latencies: Add 2, Mult 10, Div 40 clocks

## Slide 7: Three Stages of Tomasulo Algorithm
Issue—get instruction from FP Op Queue
  If reservation station free (no structural hazard), control issues instr & sends operands (renames registers).
Execution—operate on operands (EX)
  When both operands ready then execute; if not ready, watch Common Data Bus for result
Write result—finish execution (WB)
  Write on Common Data Bus to all awaiting units; mark reservation station available

## Slide 8: Normal vs. Common Data Bus
Normal data bus: data + destination
  (“go to” bus)
Common data bus: data + source
  (“come from” bus)
  64 bits of data + 4 bits of Functional Unit source address
  Write if matches expected Functional Unit (produces result)
  Broadcast: one to many

## Slide 9: Tomasulo Example

## Slide 10: Tomasulo Example Cycle 1

## Slide 11: Tomasulo Example Cycle 2
Note: Unlike 6600, can have multiple loads outstanding

## Slide 12: Tomasulo Example Cycle 3
Note: registers names are removed (“renamed”) in Reservation Stations; MULT issued vs. scoreboard
Load1 completing; what is waiting for Load1?

## Slide 13: Tomasulo Example Cycle 4
Load2 completing; what is waiting for it?

## Slide 14: Tomasulo Example Cycle 5

## Slide 15: Tomasulo Example Cycle 6
Issue ADDD here vs. scoreboard?

## Slide 16: Tomasulo Example Cycle 7
Add1 completing; what is waiting for it?

## Slide 17: Tomasulo Example Cycle 8

## Slide 18: Tomasulo Example Cycle 9

## Slide 19: Tomasulo Example Cycle 10
Add2 completing; what is waiting for it?

## Slide 20: Tomasulo Example Cycle 11
Write result of ADDD here vs. scoreboard?

## Slide 21: Tomasulo Example Cycle 12
Note: all quick instructions complete already

## Slide 22: Tomasulo Example Cycle 13

## Slide 23: Tomasulo Example Cycle 14

## Slide 24: Tomasulo Example Cycle 15
Mult1 completing; what is waiting for it?

## Slide 25: Tomasulo Example Cycle 16
Note: Just waiting for divide

## Slide 26: Tomasulo Example Cycle 55

## Slide 27: Tomasulo Example Cycle 56
Mult 2 completing; what is waiting for it?

## Slide 28: Tomasulo Example Cycle 57
Again, in-order issue, out-of-order execution, completion

## Slide 29: Compare to Scoreboard
Why longer on Scoreboard/6600?

## Slide 30: Tomasulo vs. Scoreboard
Tomasulo Drawbacks
  Circuit complexity
  Many associative stores (CDB) at high speed
  Performance limited by Common Data Bus
    Multiple CDBs  more FU logic for parallel associative stores

## Slide 31: Tomasulo Loop Example
Loop: LD F0, 0(R1)
MULTD F4, F0, F2
SD F4, 0(R1)
SUBI R1, R1, #8
BNEZ R1, Loop
Assume Multiply takes 4 clocks
Assume first load takes 8 clocks (cache miss), second load takes 4 clocks (hit)
To be clear, will show clocks for SUBI, BNEZ
Reality, integer instructions ahead

## Slide 32: Loop Example Cycle 0

## Slide 33: Loop Example Cycle 1

## Slide 34: Loop Example Cycle 2

## Slide 35: Loop Example Cycle 3
Note: MULT1 has no registers names in RS

## Slide 36: Loop Example Cycle 4
Issue SUBI

## Slide 37: Loop Example Cycle 5
Issue BNEZ

## Slide 38: Loop Example Cycle 6
Note: F0 never sees Load1 result

## Slide 39: Loop Example Cycle 7
Note: MULT2 has no registers names in RS

## Slide 40: Loop Example Cycle 8

## Slide 41: Loop Example Cycle 9
Load1 completing; what is waiting for it?

## Slide 42: Loop Example Cycle 10
Load2 completing; what is waiting for it?

## Slide 43: Loop Example Cycle 11

## Slide 44: Loop Example Cycle 12

## Slide 45: Loop Example Cycle 13

## Slide 46: Loop Example Cycle 14
Mult1 completing; what is waiting for it?

## Slide 47: Loop Example Cycle 15
Mult2 completing; what is waiting for it?

## Slide 48: Loop Example Cycle 16

## Slide 49: Loop Example Cycle 17

## Slide 50: Loop Example Cycle 18

## Slide 51: Loop Example Cycle 19

## Slide 52: Loop Example Cycle 20

## Slide 53: Loop Example Cycle 21

## Slide 54: Multiple Issue
Static: Integer/FP instruction pairs
Dynamic: Extend Tomasulo
  Must handle dependencies on issue
  Two instructions: split clock in half
  More: Explicit dependency issue logic
    E.g. 2 in 1st half of clock, 2 in 2nd half

## Slide 55: Reorder Buffers
Most modern processors use a variation of Tomasulo
Add Reorder Buffer (ROB) at end
Write registers from ROB in order
Makes sure earlier instructions complete
  Simplifies exceptions & speculation