## Slide 1: CMSC 611: Advanced Computer Architecture
Design & Simulation Languages
Practically everything adapted from slides by Peter J. Ashenden, VHDL Quick Start
Some material adapted from Mohamed Younis, UMBC CMSC 611 Spr 2003 course slides

## Slide 2: Abstraction Hierarchy of Digital Design
Digital designers often employ abstraction hierarchy, which can be expressed in two domains:
  Structural domain: Components are described in terms of an interconnection of more primitive components
  Behavior domain: Components are described by defining the their input/output responses by means of a procedure

## Slide 3: Design's Levels of Abstraction
Notes: PMS = Processor, Memory, Switch

## Slide 4: Domains and Levels of Modeling
high level of abstraction
Functional
Structural
Geometric
“Y-chart” due to Gajski & Kahn
low level of abstraction

## Slide 5: Domains and Levels of Modeling
Functional
Structural
Geometric
Algorithm (behavioral)
Register-Transfer Language
Boolean Equation
Differential Equation
“Y-chart” due to Gajski & Kahn

## Slide 6: Domains and Levels of Modeling
Functional
Structural
Geometric
Processor-Memory Switch
Register-Transfer
Gate
Transistor
“Y-chart” due to Gajski & Kahn

## Slide 7: Domains and Levels of Modeling
Functional
Structural
Geometric
Polygons
Sticks
Standard Cells
Floor Plan
“Y-chart” due to Gajski & Kahn

## Slide 8: Functional Simulator
Program simulating behavior of design
  Match interfaces
  Use any language or algorithm
Can use to develop external HW or SW
Graphics examples
  SGI modified software OpenGL
  UNC process-per-board
CPU examples
  SimpleScalar, Valgrind

## Slide 9: Hardware Design Languages
A hardware design language provides primitives for describing both structural and behavioral models of the design
Hardware design languages are useful in
  Documenting and modeling the design
  Ensuring design portability
Every hardware design language is supported by a simulator that helps in:
  Validating the design
  Mitigating the risk of design faults
  Avoiding expensive prototyping for complicated hardware

## Slide 10: VHDL & Verilog
VHDL and Verilog are the most famous and widely used hardware design language
Focus on VHDL:
  Interfaces, Behavior, Structure, Test Benches
  Analysis, Elaboration, Simulation, Synthesis

## Slide 11: Modeling Digital Systems
VHDL is for writing models of a system
Reasons for modeling
  requirements specification
  documentation
  testing using simulation
  formal verification
  synthesis
Goal
  most reliable design process, with minimum cost and time
  avoid design errors!

## Slide 12: Modeling Interfaces
Entity declaration
  describes the input/output ports of a module
entity reg4 is port ( d0, d1, d2, d3, en, clk : in bit; q0, q1, q2, q3 : out bit ); end reg4;
entity name
port names
port mode (direction)
port type

## Slide 13: Modeling Behavior
Architecture body
  describes an implementation of an entity
  may be several per entity
Behavioral architecture
  describes the algorithm performed by the module
  contains
    process statements, each containing
    sequential statements, including
    signal assignment statements and
    wait statements

## Slide 14: Behavior Example
architecture behav of reg4 is begin
storage : process is variable stored_d0, stored_d1, stored_d2, stored_d3 : bit; begin if en = '1' and clk = '1' then stored_d0 := d0; stored_d1 := d1; stored_d2 := d2; stored_d3 := d3; end if; q0 <= stored_d0 after 5 ns; q1 <= stored_d1 after 5 ns; q2 <= stored_d2 after 5 ns; q3 <= stored_d3 after 5 ns; wait on d0, d1, d2, d3, en, clk; end process storage;
end architecture behav;

## Slide 15: Modeling Structure
Structural architecture
  implements the module as a composition of subsystems
  contains
    signal declarations, for internal interconnections
      the entity ports are also treated as signals
    component instances
      instances of previously declared entity/architecture pairs
    port maps in component instances
      connect signals to component ports
    wait statements

## Slide 16: Structure Example
int_clk
d0
d1
d2
d3
en
clk
q0
q1
q2
q3
bit0
d_latch
d
clk
q
bit1
d_latch
d
clk
q
bit2
d_latch
d
clk
q
bit3
d_latch
d
clk
q
gate
and2
a
b
y

## Slide 17: Structure Example
First declare D-latch and and-gate entities and architectures
entity d_latch is port ( d, clk : in bit; q : out bit ); end entity d_latch;
architecture basic of d_latch is begin
latch_behavior : process is begin if clk = ‘1’ then q <= d after 2 ns; end if; wait on clk, d; end process latch_behavior;
end architecture basic;
entity and2 is port ( a, b : in bit; y : out bit ); end entity and2;
architecture basic of and2 is begin
and2_behavior : process is begin y <= a and b after 2 ns; wait on a, b; end process and2_behavior;
end architecture basic;

## Slide 18: Structure Example
Now use them to implement a register
architecture struct of reg4 is
signal int_clk : bit;
begin
bit0 : entity work.d_latch(basic) port map ( d0, int_clk, q0 );
bit1 : entity work.d_latch(basic) port map ( d1, int_clk, q1 );
bit2 : entity work.d_latch(basic) port map ( d2, int_clk, q2 );
bit3 : entity work.d_latch(basic) port map ( d3, int_clk, q3 );
gate : entity work.and2(basic) port map ( en, clk, int_clk );
end architecture struct;

## Slide 19: Mixed Behavior and Structure
An architecture can contain both behavioral and structural parts
  process statements and component instances
    collectively called concurrent statements
  processes can read and assign to signals
Example: register-transfer-level model
  data path described structurally
  control section described behaviorally

## Slide 20: Mixed Example
shift_reg
reg
shift_
adder
control_
section
multiplier
multiplicand
product

## Slide 21: Mixed Example
entity multiplier is port ( clk, reset : in bit; multiplicand, multiplier : in integer; product : out integer ); end entity multiplier;
architecture mixed of multiplier is
signal partial_product, full_product : integer; signal arith_control, result_en, mult_bit, mult_load : bit;
begin
arith_unit : entity work.shift_adder(behavior) port map ( addend => multiplicand, augend => full_product, sum => partial_product, add_control => arith_control );
result : entity work.reg(behavior) port map ( d => partial_product, q => full_product, en => result_en, reset => reset );
...

## Slide 22: Mixed Example
…
multiplier_sr : entity work.shift_reg(behavior) port map ( d => multiplier, q => mult_bit, load => mult_load, clk => clk );
product <= full_product;
control_section : process is -- variable declarations for control_section -- … begin -- sequential statements to assign values to control signals -- … wait on clk, reset; end process control_section;
end architecture mixed;

## Slide 23: Design Simulator
Simulation continues until the event queue is empty or stopped externally by
the designer
Device behavioral model is represented by procedure calls
Events within the simulator are kept in a time-based queue
Events stored as three-tuples (Module #, Pin #, New logic value)
Depending on the behavioral model of a module, the handling of an event usually trigger other events that will be inserted in the event queue

## Slide 24: Test Benches
Testing a design by simulation
Use a test bench model
  an architecture body that includes an instance of the design under test
  applies sequences of test values to inputs
  monitors values on output signals
    either using simulator
    or with a process that verifies correct operation

## Slide 25: Test Bench Example
entity test_bench is end entity test_bench;
architecture test_reg4 of test_bench is
signal d0, d1, d2, d3, en, clk, q0, q1, q2, q3 : bit;
begin
dut : entity work.reg4(behav) port map ( d0, d1, d2, d3, en, clk, q0, q1, q2, q3 );
stimulus : process is begin d0 <= ’1’; d1 <= ’1’; d2 <= ’1’; d3 <= ’1’; wait for 20 ns; en <= ’0’; clk <= ’0’; wait for 20 ns; en <= ’1’; wait for 20 ns; clk <= ’1’; wait for 20 ns; d0 <= ’0’; d1 <= ’0’; d2 <= ’0’; d3 <= ’0’; wait for 20 ns; en <= ’0’; wait for 20 ns; … wait; end process stimulus;
end architecture test_reg4;

## Slide 26: Regression Testing
Test that a refinement of a design is correct
  that lower-level structural model does the same as a behavioral model
Test bench includes two instances of design under test
  behavioral and lower-level structural
  stimulates both with same inputs
  compares outputs for equality
Need to take account of timing differences

## Slide 27: Regression Test Example
architecture regression of test_bench is
signal d0, d1, d2, d3, en, clk : bit; signal q0a, q1a, q2a, q3a, q0b, q1b, q2b, q3b : bit;
begin
dut_a : entity work.reg4(struct) port map ( d0, d1, d2, d3, en, clk, q0a, q1a, q2a, q3a );
dut_b : entity work.reg4(behav) port map ( d0, d1, d2, d3, en, clk, q0b, q1b, q2b, q3b );
stimulus : process is begin d0 <= ’1’; d1 <= ’1’; d2 <= ’1’; d3 <= ’1’; wait for 20 ns; en <= ’0’; clk <= ’0’; wait for 20 ns; en <= ’1’; wait for 20 ns; clk <= ’1’; wait for 20 ns; … wait; end process stimulus;
...

## Slide 28: Regression Test Example
…
verify : process is begin wait for 10 ns; assert q0a = q0b and q1a = q1b and q2a = q2b and q3a = q3b report ”implementations have different outputs” severity error; wait on d0, d1, d2, d3, en, clk; end process verify;
end architecture regression;

## Slide 29: Design Processing
Analysis
Elaboration
Simulation
Synthesis

## Slide 30: Analysis
Check for syntax and semantic errors
  syntax: grammar of the language
  semantics: the meaning of the model
Analyze each design unit separately
  entity declaration
  architecture body
  …
  best if each design unit is in a separate file
Analyzed design units are placed in a library
  in an implementation dependent internal form
  current library is called work

## Slide 31: Elaboration
“Flattening” the design hierarchy
  create ports
  create signals and processes within architecture body
  for each component instance, copy instantiated entity and architecture body
  repeat recursively
    bottom out at purely behavioral architecture bodies
Final result of elaboration
  flat collection of signal nets and processes

## Slide 32: Elaboration Example
int_clk
d0
d1
d2
d3
en
clk
q0
q1
q2
q3
bit0
d_latch
d
clk
q
bit1
d_latch
d
clk
q
bit2
d_latch
d
clk
q
bit3
d_latch
d
clk
q
gate
and2
a
b
y
reg4(struct)

## Slide 33: Elaboration Example
int_clk
d0
d1
d2
d3
en
clk
q0
q1
q2
q3
bit0
bit1
bit2
bit3
gate
reg4(struct)
d_latch(basic)
d
clk
q
d_latch(basic)
d
clk
q
d_latch(basic)
d
clk
q
d_latch(basic)
d
clk
q
and2(basic)
a
b
y
process with variables and statements

## Slide 34: Simulation
Execution of the processes in the elaborated model
Discrete event simulation
  time advances in discrete steps
  when signal values change—events
A processes is sensitive to events on input signals
  specified in wait statements
  resumes and schedules new values on output signals
    schedules transactions
    event on a signal if new value different from old value

## Slide 35: Simulation Algorithm
Initialization phase
  each signal is given its initial value
  simulation time set to 0
  for each process
    activate
    execute until a wait statement, then suspend
      execution usually involves scheduling transactions on signals for later times

## Slide 36: Simulation Algorithm
Simulation cycle
  advance simulation time to time of next transaction
  for each transaction at this time
    update signal value
      event if new value is different from old value
  for each process sensitive to any of these events, or whose “wait for …” time-out has expired
    resume
    execute until a wait statement, then suspend
Simulation finishes when there are no further scheduled transactions

## Slide 37: Synthesis
Translates register-transfer-level (RTL) design into gate-level netlist
Restrictions on coding style for RTL model
Tool dependent

## Slide 38: Basic Design Methodology
Requirements
Simulate
RTL Model
Gate-level Model
Synthesize
Simulate
Test Bench
ASIC or FPGA
Place & Route
Timing Model
Simulate