## Slide 1: CMSC 611: Advanced Computer Architecture
Pipelining
Some material adapted from Mohamed Younis, UMBC CMSC 611 Spr 2003 course slides
Some material adapted from Hennessy & Patterson / © 2003 Elsevier Science

## Slide 2: Sequential Laundry
Washer takes 30 min, Dryer takes 40 min, folding takes 20 min
Sequential laundry takes 6 hours for 4 loads
If they learned pipelining, how long would laundry take?
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
Slide: Dave Patterson
Time
A
B
C
D
T
a
s
k
O
r
d
e
r

## Slide 3: Pipelined Laundry
Pipelining means start work as soon as possible
Pipelined laundry takes 3.5 hours for 4 loads
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20
Slide: Dave Patterson

## Slide 4: Pipelining Lessons
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Pipeline rate limited by slowest pipeline stage
Multiple tasks operating simultaneously using different resources
Potential speedup = Number pipe stages
Unbalanced lengths of pipe stages reduces speedup
Time to “fill” pipeline and time to “drain” it reduce speedup
Stall for Dependencies
Time
6 PM
7
8
9
Slide: Dave Patterson
A
B
C
D
T
a
s
k
O
r
d
e
r
30
40
40
40
40
20

## Slide 5: MIPS Instruction Set
op
target address
0
26
31
6 bits
26 bits
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
RISC architecture:
  ALU operations only on registers
  Memory is affected only by load and store
  Instructions follow very few formats and typically are of the same size

## Slide 6: Single Cycle Execution

## Slide 7: Single Cycle Execution

## Slide 8: Single Cycle Execution

## Slide 9: Single Cycle Execution

## Slide 10: Single Cycle Execution

## Slide 11: Single Cycle Execution

## Slide 12: Single Cycle Execution

## Slide 13: Single Cycle Execution

## Slide 14: Single Cycle Execution

## Slide 15: Single Cycle Execution

## Slide 16: Single Cycle Execution

## Slide 17: Multi-Cycle Execution

## Slide 18: Multi-Cycle Implementation of MIPS
Instruction fetch cycle (IF)
IR  Mem[PC]; NPC  PC + 4
Instruction decode/register fetch cycle (ID)
A  Regs[IR6..10]; B  Regs[IR11..15]; Imm  ((IR16)16 ##IR16..31)
Execution/effective address cycle (EX)
Memory ref: ALUOutput  A + Imm;
  Reg-Reg ALU: ALUOutput  A func B;
  Reg-Imm ALU: ALUOutput  A op Imm;
  Branch: ALUOutput  NPC + Imm; Cond  (A op 0)
Memory access/branch completion cycle (MEM)
  Memory ref: LMD  Mem[ALUOutput] or Mem(ALUOutput]  B;
  Branch: if (cond) PC ALUOutput;
Write-back cycle (WB)
  Reg-Reg ALU: Regs[IR16..20]  ALUOutput;
  Reg-Imm ALU: Regs[IR11..15]  ALUOutput;
  Load: Regs[IR11..15]  LMD;

## Slide 19: Single Cycle
Cycle time long enough for longest instruction
Shorter instructions waste time
No overlap
Clk
Load
Store
Waste
Cycle 1
Cycle 2
Figure: Dave Patterson
Notes: Here are the timing diagrams showing the differences between the single cycle, multiple cycle, and pipeline implementations.
For example, in the pipeline implementation, we can finish executing the Load, Store, and R-type instruction sequence in seven cycles.
In the multiple clock cycle implementation, however, we cannot start executing the store until Cycle 6 because we must wait for the load instruction to complete.
Similarly, we cannot start the execution of the R-type instruction until the store instruction has completed its execution in Cycle 9.
In the Single Cycle implementation, the cycle time is set to accommodate the longest instruction, the Load instruction.
Consequently, the cycle time for the Single Cycle implementation can be five times longer than the multiple cycle implementation.
But may be more importantly, since the cycle time has to be long enough for the load instruction, it is too long for the store instruction so the last part of the cycle here is wasted.
+2 = 77 min. (X:57)

## Slide 20: Multiple Cycle
Figure: Dave Patterson
Cycle time long enough for longest stage
Shorter stages waste time
Shorter instructions can take fewer cycles
No overlap
Cycle 1
Ifetch
Reg
Exec
Mem
Wr
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
Ifetch
Reg
Exec
Mem
Load
Store
Ifetch
R-type
Clk
Notes: Here are the timing diagrams showing the differences between the single cycle, multiple cycle, and pipeline implementations.
For example, in the pipeline implementation, we can finish executing the Load, Store, and R-type instruction sequence in seven cycles.
In the multiple clock cycle implementation, however, we cannot start executing the store until Cycle 6 because we must wait for the load instruction to complete.
Similarly, we cannot start the execution of the R-type instruction until the store instruction has completed its execution in Cycle 9.
In the Single Cycle implementation, the cycle time is set to accommodate the longest instruction, the Load instruction.
Consequently, the cycle time for the Single Cycle implementation can be five times longer than the multiple cycle implementation.
But may be more importantly, since the cycle time has to be long enough for the load instruction, it is too long for the store instruction so the last part of the cycle here is wasted.
+2 = 77 min. (X:57)

## Slide 21: Stages of Instruction Execution
The load instruction is the longest
All instructions follows at most the following five steps:
  Ifetch: Instruction Fetch
    Fetch the instruction from the Instruction Memory and update PC
  Reg/Dec: Registers Fetch and Instruction Decode
  Exec: Calculate the memory address
  Mem: Read the data from the Data Memory
  WB: Write the data back to the register file
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Ifetch
Reg/Dec
Exec
Mem
WB
Load
Slide: Dave Patterson
Notes: As shown here, each of these five steps will take one clock cycle to complete.
And in pipeline terminology, each step is referred to as one stage of the pipeline.
+1 = 8 min. (X:48)

## Slide 22: Pipeline
Figure: Dave Patterson
Cycle time long enough for longest stage
Shorter stages waste time
No additional benefit from shorter instructions
Overlap instruction execution
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
Clk
Load
Ifetch
Reg
Exec
Mem
Wr
Ifetch
Reg
Exec
Mem
Wr
Store
Ifetch
Reg
Exec
Mem
Wr
R-type
Notes: Here are the timing diagrams showing the differences between the single cycle, multiple cycle, and pipeline implementations.
For example, in the pipeline implementation, we can finish executing the Load, Store, and R-type instruction sequence in seven cycles.
In the multiple clock cycle implementation, however, we cannot start executing the store until Cycle 6 because we must wait for the load instruction to complete.
Similarly, we cannot start the execution of the R-type instruction until the store instruction has completed its execution in Cycle 9.
In the Single Cycle implementation, the cycle time is set to accommodate the longest instruction, the Load instruction.
Consequently, the cycle time for the Single Cycle implementation can be five times longer than the multiple cycle implementation.
But may be more importantly, since the cycle time has to be long enough for the load instruction, it is too long for the store instruction so the last part of the cycle here is wasted.
+2 = 77 min. (X:57)

## Slide 23: Multi-Cycle Execution

## Slide 24: Pipeline

## Slide 25: Instruction Pipelining
IFetch
Dec
Exec
Mem
WB
IFetch
Dec
Exec
Mem
WB
IFetch
Dec
Exec
Mem
WB
IFetch
Dec
Exec
Mem
WB
IFetch
Dec
Exec
Mem
WB
IFetch
Dec
Exec
Mem
WB
Program Flow
Time
Pipelining improves performance by increasing instruction throughput
Start handling next instruction while the current instruction is in progress
Feasible when different devices at different stages

## Slide 26: Example of Instruction Pipelining
Ideal and upper bound for speedup is number of stages in the pipeline
Time between first & fourth instructions is 3  2 = 6 ns
Time between first & fourth instructions is 3  8 = 24 ns

## Slide 27: Pipeline Performance
Pipeline increases the instruction throughput
  not execution time of an individual instruction
An individual instruction can be slower:
  Additional pipeline control
  Imbalance among pipeline stages
Suppose we execute 100 instructions:
  Single Cycle Machine
    45 ns/cycle x 1 CPI x 100 inst = 4500 ns
  Multi-cycle Machine
    10 ns/cycle x 4.2 CPI (due to inst mix) x 100 inst = 4200 ns
  Ideal 5 stages pipelined machine
    10 ns/cycle x (1 CPI x 100 inst + 4 cycle drain) = 1040 ns
Lose performance due to fill and drain

## Slide 28: Pipeline Datapath
Data Stationary
Every stage must be completed in one clock cycle to avoid stalls
Values must be latched to ensure correct execution of instructions
The PC multiplexer has moved to the IF stage to prevent two instructions from updating the PC simultaneously (in case of branch instruction)

## Slide 29: Pipeline Stage Interface

## Slide 30: Pipeline Hazards
Cases that affect instruction execution semantics and thus need to be detected and corrected
Hazards types
  Structural hazard: attempt to use a resource two different ways at same time
    Single memory for instruction and data
  Data hazard: attempt to use item before it is ready
    Instruction depends on result of prior instruction still in the pipeline
  Control hazard: attempt to make a decision before condition is evaluated
    branch instructions
Hazards can always be resolved by waiting

## Slide 31: Visualizing Pipelining
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Slide: David Culler

## Slide 32: Example: One Memory Port/Structural Hazard
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Instr 3
Instr 4
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
DMem
Structural Hazard
Slide: David Culler

## Slide 33: Resolving Structural Hazards
Wait
  Must detect the hazard
    Easier with uniform ISA
  Must have mechanism to stall
    Easier with uniform pipeline organization
Throw more hardware at the problem
  Use instruction & data cache rather than direct access to memory

## Slide 34: Detecting and Resolving Structural Hazard
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Stall
Instr 3
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg
Bubble
Bubble
Bubble
Bubble
Bubble
Slide: David Culler

## Slide 35: Stalls & Pipeline Performance
Assuming all pipeline stages are balanced