## Slide 1: CMSC 611: Advanced Computer Architecture
Memory & Virtual Memory
Some material adapted from Mohamed Younis, UMBC CMSC 611 Spr 2003 course slides
Some material adapted from Hennessy & Patterson / © 2003 Elsevier Science

## Slide 2: Memory Hierarchy
CPU Registers
100s Bytes
<10s ns
Cache
K-M Bytes
10-40 ns
Main Memory
G Bytes
70ns-1us
Disk
G-T Bytes
ms
Capacity
Access Time
Registers
Cache
Main Memory
Disk
Instr. Operands
Blocks
Pages
Staging
Transfer Unit
Prog./compiler
1-8 bytes
cache cntl
8-128 bytes
OS
512-4K bytes
Upper Level
Lower Level
faster
Larger

## Slide 3: Main Memory Background
Performance of Main Memory:
  Latency: affects cache miss penalty
    Access Time: time between request and word arrives
    Cycle Time: time between requests
  Bandwidth: primary concern for I/O & large block
Main Memory is DRAM: Dynamic RAM
  Dynamic since needs to be refreshed periodically
  Addresses divided into 2 halves (Row/Column)
Cache uses SRAM: Static RAM
  No refresh
    6 transistors/bit vs. 1 transistor/bit, 10X area
  Address not divided: Full address

## Slide 4: DRAM Logical Organization
4 Mbit DRAM:
square root of bits per RAS/CAS
Refreshing prevent access to the DRAM (typically 1-5% of the time)
Reading one byte refreshes the entire row
Read is destructive and thus data need to be re-written after reading
  Cycle time is significantly larger than access time

## Slide 5: Processor-Memory Performance
µProc
60%/yr.
(2X/1.5yr)
DRAM
9%/yr.
(2X/10 yrs)
1
10
100
1000
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
DRAM
CPU
1982
Processor-Memory
Performance Gap: (grows 50% / year)
Performance
Time
CPU-DRAM Gap“Moore’s Law”
Problem:
  Improvements in access time are not enough to catch up
Solution:
  Increase the bandwidth of main memory (improve throughput)

## Slide 6: Memory Organization
Simple: CPU, Cache, Bus, Memory same width (32 bits)
Wide: CPU/Mux 1 word; Mux/Cache, Bus, Memory N words
Interleaved: CPU, Cache, Bus 1 word: Memory N Modules (4 Modules); example is word interleaved
Memory organization would have significant effect on bandwidth

## Slide 7: Memory Interleaving
Start Access for D1
CPU
Memory
Start Access for D2
D1 available
Access Bank 0
We can Access Bank 0 again
CPU
Memory
Bank 1
Memory
Bank 0
Memory
Bank 3
Memory
Bank 2
Access Bank 1
Access Bank 2
Access Bank 3
Access Pattern without Interleaving:
Access Pattern with 4-way Interleaving:

## Slide 8: Virtual Memory
Cache Virtual memory
Block  Page
Cache miss  page fault
Block  Address
addressing translation
Using virtual addressing, main memory plays the role of cache for disks
The virtual space is much larger than the physical memory space
Physical main memory contains only the active portion of the virtual space
Address space can be divided into fixed size (pages) or variable size (segments) blocks

## Slide 9: Virtual Memory
Cache Virtual memory
Block  Page
Cache miss  page fault
Block  Address
addressing translation
Advantages
  Allows efficient and safe data sharing of memory among multiple programs
  Moves programming burdens of a small, limited amount of main memory
  Simplifies program loading and avoid the need for contiguous memory block
  allows programs to be loaded at any physical memory location

## Slide 10: Virtual Addressing
Page faults are costly and take millions of cycles to process (disks are slow)
Optimization Strategies:
  Pages should be large enough to amortize the access time
  Fully associative placement of pages reduces page fault rate
  Software-based so can use clever page placement
  Write-through can make writing very time consuming (use copy back)

## Slide 11: Page Table
Hardware supported
Page table:
  Resides in main memory
  One entry per virtual page
  No tag is requires since it covers all virtual pages
  Point directly to physical page
  Table can be very large
  Operating sys. may maintain one page table per process
  A dirty bit is used to track modified pages for copy back

## Slide 12: Page Faults
A page fault happens when the valid bit of a virtual page is off
A page fault generates an exception to be handled by the operating system to bring the page to main memory from a disk
The operating system creates space for all pages on disk and keeps track of the location of pages in main memory and disk
Page location on disk can be stored in page table or in an auxiliary structure
LRU page replacement strategy is the most common
Simplest LRU implementation uses a reference bit per page and periodically reset reference bits

## Slide 13: Optimizing Page Table Size
With a 32-bit virtual address, 4-KB pages, and 4 bytes per page table entry:
Optimization techniques:
  Keep bound registers to limit the size of page table for given process in order to avoid empty slots
  Store only physical pages and apply hashing function of the virtual address (inverted page table)
  Use multi-level page table to limit size of the table residing in main memory
  Allow paging of the page table
  Cache the most used pages  Translation Look-aside Buffer

## Slide 14: Multi-Level Page Table
32-bit address:
P1 index
P2 index
page offest
10
10
12
4 bytes
4 bytes
4KB
1K
PTEs
° 2 GB virtual address space
° 4 MB of PTE2
– paged, holes
° 4 KB of PTE1
Inverted page table can be the only practical solution for huge address space, e.g 64-bit address space

## Slide 15: Translation Look-aside Buffer
Special cache for recently used translation
TLB misses are typically handled as exceptions by operating system
Simple replacement strategy since TLB misses happen frequently