## Slide 1: CMSC 611: Advanced Computer Architecture
Parallel Computation
Most slides adapted from David Patterson. Some from Mohomed Younis

## Slide 2: Parallel Computers
Definition: “A parallel computer is a collection of processing elements that cooperate and communicate to solve large problems fast.”
  Almasi and Gottlieb, Highly Parallel Computing,1989
Parallel machines have become increasingly important since:
  Power & heat problems grow for big/fast processors
  Even with double transistors, how do you use them to make a single processor faster?
  CPUs are being developed with an increasing number of cores

## Slide 3: Questions about parallel computers:
How large a collection?
How powerful are processing elements?
How do they cooperate and communicate?
How are data transmitted?
What type of interconnection?
What are HW and SW primitives for programmers?
Does it translate into performance?

## Slide 4: Level of Parallelism
Bit-level parallelism
  ALU parallelism: 1-bit, 4-bits, 8-bit, ...
Instruction-level parallelism (ILP)
  Pipelining, Superscalar, VLIW, Out-of-Order execution
Process/Thread-level parallelism
  Divide job into parallel tasks
Job-level parallelism
  Independent jobs on one computer system

## Slide 5: Applications
App | Perf (GFLOPS) | Memory (GB)
48 hour weather | 0.1 | 0.1
72 hour weather | 3 | 1
Pharmaceutical design | 100 | 10
Global Change, Genome | 1000 | 1000
Scientific Computing
  Nearly Unlimited Demand (Grand Challenge):
  Successes in some real industries:
    Petroleum: reservoir modeling
    Automotive: crash simulation, drag analysis, engine
    Aeronautics: airflow analysis, engine, structural mechanics
    Pharmaceuticals: molecular modeling

## Slide 6: Commercial Applications
Transaction processing
File servers
Electronic CAD simulation
Large WWW servers
WWW search engines
Graphics
  Graphics hardware
  Render Farms

## Slide 7: Framework
Extend traditional computer architecture with a communication architecture
  abstractions (HW/SW interface)
  organizational structure to realize abstraction efficiently
Programming Model:
  Multiprogramming: lots of jobs, no communication
  Shared address space: communicate via memory
  Message passing: send and receive messages
  Data Parallel: operate on several data sets simultaneously and then exchange information globally and simultaneously (shared or message)

## Slide 8: Communication Abstraction
Shared address space:
  e.g., load, store, atomic swap
Message passing:
  e.g., send, receive library calls
Debate over this topic (ease of programming, scaling)
  many hardware designs 1:1 programming model

## Slide 9: Taxonomy of Parallel Architecture
Flynn Categories
  SISD (Single Instruction Single Data)
  MIMD (Multiple Instruction Multiple Data)
  MISD (Multiple Instruction Single Data)
  SIMD (Single Instruction Multiple Data)

## Slide 10: SISD
Uniprocessor

## Slide 11: MIMD
Multiple communicating processes

## Slide 12: MISD
No commercial examples
Different operations to a single data set
  Find primes
  Crack passwords

## Slide 13: SIMD
Vector/Array computers

## Slide 14: SIMD Arrays
Performance keys
  Utilization
  Communication

## Slide 15: Data Parallel Model
Operations performed in parallel on each element of a large regular data structure, such as an array
  One Control Processor broadcast to many processing elements (PE) with condition flag per PE so that can skip
For distributed memory architecture data is distributed among memories
  Data parallel model requires fast global synchronization
  Data parallel programming languages lay out data to processor
  Vector processors have similar ISAs, but no data placement restriction

## Slide 16: SIMD Utilization
Conditional Execution
  PE Enable
    if (f<.5) {...}
  Global enable check
    while (t > 0) {...}

## Slide 17: Communication: MasPar MP1
Fast local X-net
Slow global routing

## Slide 18: Communication: CM2
Hypercube local routing
Wormhole global routing

## Slide 19: Data Parallel Languages
SIMD programming
  PE point of view
  Data: shared or per-PE
    What data is distributed?
    What is shared over PE subset
    What data is broadcast with instruction stream?
  Data layout: shape [256][256]d;
  Communication primitives
  Higher-level operations
    Scan/Prefix sum: [i]r = ∑j≤i [j]d
      1,1,2,3,4 → 1,1+1=2,2+2=4,4+3=7,7+4=11

## Slide 20: Single Program Multiple Data
Many problems do not map well to SIMD
  Better utilization from MIMD or ILP
Data parallel model ⇒ Single Program Multiple Data (SPMD) model
  All processors execute identical program
  Same program for SIMD, SISD or MIMD
  Compiler handles mapping to architecture

## Slide 21: MIMD
Can support either SW model on either HW basis
Message Passing
Shared memory/distributed memory
  Uniform Memory Access (UMA)
  Non-Uniform Memory Access (NUMA)

## Slide 22: Message passing
Processors have private memories, communicate via messages
Advantages:
  Less hardware, easier to design
  Focuses attention on costly non-local operations

## Slide 23: Message Passing Model
Each PE has local processor, data, (I/O)
  Explicit I/O to communicate with other PEs
  Essentially NUMA but integrated at I/O vs. memory system
Free run between Send & Receive
  Send + Receive = Synchronization between processes (event model)
    Send: local buffer, remote receiving process/port
    Receive: remote sending process/port, local buffer

## Slide 24: History of message passing
Early machines
  Local communication
  Blocking send & receive
Later: DMA with non-blocking sends
  DMA for receive into buffer until processor does receive, and then data is transferred to local memory
Later still: SW libraries to allow arbitrary communication