## Slide 1: CMSC 611: Advanced Computer Architecture
Shared Memory
Most slides adapted from David Patterson. Some from Mohomed Younis

## Slide 2: Shared Memory
Processors communicate with shared address space
Easy on small-scale machines
Advantages:
  Model of choice for uniprocessors, small-scale multiprocessor
  Ease of programming
  Lower latency
  Easier to use hardware controlled caching
Difficult to handle node failure

## Slide 3: Centralized Shared Memory
Processors share a single centralized (UMA) memory through a bus interconnect
Feasible for small processor count to limit memory contention
Model for multi-core CPUs

## Slide 4: Distributed Memory
Uses physically distributed (NUMA) memory to support large processor counts (to avoid memory contention)
Advantages
  Allows cost-effective way to scale the memory bandwidth
  Reduces memory latency
Disadvantage
  Increased complexity of communicating data

## Slide 5: Shared Address Model
Physical locations
  Each PE can name every physical location in the machine
Shared data
  Each process can name all data it shares with other processes

## Slide 6: Shared Address Model
Data transfer
  Use load and store, VM maps to local or remote location
  Extra memory level: cache remote data
  Significant research on making the translation transparent and scalable for many nodes
    Handling data consistency and protection challenging
    Latency depends on the underlying hardware architecture (bus bandwidth, memory access time and support for address translation)
    Scalability is limited given that the communication model is so tightly coupled with process address space

## Slide 7: Three Fundamental Issues (#1: Naming)
What data is shared?
How it is addressed?
What operations can access data?
How processes refer to each other?
Choice of naming affects code produced by a compiler
  Just remember and load address or keep track of processor number and local virtual address for message passing
Choice of naming affects replication of data
  In cache memory hierarchy or via SW replication and consistency

## Slide 8: Naming Address Spaces
Global physical address space
  any processor can generate, address and access it in a single operation
Global virtual address space
  if the address space of each process can be configured to contain all shared data of the parallel program
    memory can be anywhere: virtual address translation handles it
Segmented shared address space
  locations are named <process number, address> uniformly for all processes of the parallel program

## Slide 9: Three Fundamental Issues (#2: Synchronization)
To cooperate, processes must coordinate
Message passing is implicit coordination with transmission or arrival of data
Shared address → additional operations to explicitly coordinate: e.g., write a flag, awaken a thread, interrupt a processor

## Slide 10: Three Fundamental Issues (#3: Latency & Bandwidth)
Bandwidth
  Need high bandwidth in communication
  Match limits in network, memory, and processor
  Overhead to communicate is a problem in many machines
Latency
  Affects performance, since processor may have to wait
  Affects ease of programming, since requires more thought to overlap communication and computation
Latency Hiding
  How can a mechanism help hide latency?
  Examples: overlap message send with computation, pre-fetch data, switch to other tasks

## Slide 11: Centralized Shared Memory MIMD
Processors share a single centralized memory through a bus interconnect
  Memory contention: Feasible for small # processors
  Caches serve to:
    Increase bandwidth versus bus/memory
    Reduce latency of access
    Valuable for both private data and shared data
  Access to shared data is optimized by replication
    Decreases latency
    Increases memory bandwidth
    Reduces contention
    Reduces cache coherence problems

## Slide 12: Cache Coherency
A cache coherence problem arises when the cache reflects a view of memory which is different from reality
A memory system is coherent if:
  P reads X, P writes X, no other processor writes X, P reads X
    Always returns value written by P
  P reads X, Q writes X, P reads X
    Returns value written by Q (provided sufficient W/R separation)
  P writes X, Q writes X
    Seen in the same order by all processors
Notes: Processor
b) Writes green, red stale
c) Update memory (green), red stale in cache

## Slide 13: Potential HW Coherency Solutions
Snooping Solution (Snoopy Bus)
  Send all requests for data to all processors
  Processors snoop to see if they have a copy and respond accordingly
  Requires broadcast, since caching information is at processors
  Works well with bus (natural broadcast medium)
  Dominates for small scale machines (most of the market)

## Slide 14: Potential HW Coherency Solutions
Directory-Based Schemes
  Keep track of what is being shared in one centralized place
  Distributed memory ⇒ distributed directory for scalability (avoids bottlenecks)
  Send point-to-point requests to processors via network
  Scales better than Snooping
  Actually existed before Snooping-based schemes

## Slide 15: Basic Snooping Protocols
Write Invalidate Protocol:
  Write to shared data: an invalidate is sent to all caches which snoop and invalidate any copies
  Cache invalidation will force a cache miss when accessing the modified shared item
  For multiple writers only one will win the race ensuring serialization of the write operations
  Read Miss:
    Write-through: memory is always up-to-date
    Write-back: snoop in caches to find most recent copy

## Slide 16: Basic Snooping Protocols
Write Broadcast (Update) Protocol (typically write through):
  Write to shared data: broadcast on bus, processors snoop, and update any copies
  To limit impact on bandwidth, track data sharing to avoid unnecessary broadcast of written data that is not shared
  Read miss: memory is always up-to-date
  Write serialization: bus serializes requests!

## Slide 17: Invalidate vs. Update
Write-invalidate has emerged as the winner for the vast majority of designs
Qualitative Performance Differences :
  Spatial locality
    WI: 1 transaction/cache block;
    WU: 1 broadcast/word
  Latency
    WU: lower write–read latency
    WI: must reload new value to cache

## Slide 18: Invalidate vs. Update
Because the bus and memory bandwidth is usually in demand, write-invalidate protocols are very popular
Write-update can causes problems for some memory consistency models, reducing the potential performance gain it could bring
The high demand for bandwidth in write-update limits its scalability for large number of processors

## Slide 19: An Example Snoopy Protocol
Invalidation protocol, write-back cache
Each block of memory is in one state:
  Clean in all caches and up-to-date in memory (Shared)
  OR Dirty in exactly one cache (Exclusive)
  OR Not in any caches
Each cache block is in one state (track these):
  Shared : block can be read
  OR Exclusive : cache has only copy, it is write-able, and dirty
  OR Invalid : block contains no data
Read misses: cause all caches to snoop bus
Writes to clean line are treated as misses

## Slide 20: Snoopy-Cache Controller
Complications
  Cannot update cache until bus is obtained
  Two step process:
    Arbitrate for bus
    Place miss on bus and complete operation
  Split transaction bus:
    Bus transaction is not atomic
    Multiple misses can interleave, allowing two caches to grab block in the Exclusive state
    Must track and prevent multiple misses for one block

## Slide 21: Example
Assumes memory blocks A1 and A2 map to same cache block, initial cache state is invalid

## Slide 22: Example
Assumes memory blocks A1 and A2 map to same cache block

## Slide 23: Example
Assumes memory blocks A1 and A2 map to same cache block

## Slide 24: Example
Assumes memory blocks A1 and A2 map to same cache block

## Slide 25: Example
Assumes memory blocks A1 and A2 map to same cache block

## Slide 26: Example
A1
A1
Assumes memory blocks A1 and A2 map to same cache block
Notes: Why write miss first?
Because in general, only write a piece of block, may need to read it first so that can have a full vblock; therefore, need to get
Write back is low priority event.

## Slide 27: Modern Variations
MESI(F)
  Invalid: no longer valid
  Modified (renamed vs. 3-state protocol)
    1 core can be modified, rest must be Invalid
    Data has been changed, will need to write back
  Shared
    Read only: many cores can be shared, read only
  Forward (new)
    Most recent shared core, designated to forward data
    Forwarding saves slower memory access
  Exclusive (new)
    Single read only core
    Like Forward, but can change to Modified without asking