## Slide 1: CMSC 611: Advanced Computer Architecture
Pipelining
Some material adapted from Mohamed Younis, UMBC CMSC 611 Spr 2003 course slides
Some material adapted from Hennessy & Patterson / © 2003 Elsevier Science

## Slide 2: Sequential Laundry
Washer takes 30 min, Dryer takes 40 min, folding takes 20 min
Sequential laundry takes 6 hours for 4 loads
If they learned pipelining, how long would laundry take?
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
Slide: Dave Patterson
Time
A
B
C
D
T
a
s
k
O
r
d
e
r

## Slide 3: Pipelined Laundry
Pipelining means start work as soon as possible
Pipelined laundry takes 3.5 hours for 4 loads
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20
Slide: Dave Patterson

## Slide 4: Pipelining Lessons
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Pipeline rate limited by slowest pipeline stage
Multiple tasks operating simultaneously using different resources
Potential speedup = Number pipe stages
Unbalanced lengths of pipe stages reduces speedup
Time to “fill” pipeline and time to “drain” it reduce speedup
Stall for Dependencies
Time
6 PM
7
8
9
Slide: Dave Patterson
A
B
C
D
T
a
s
k
O
r
d
e
r
30
40
40
40
40
20

## Slide 5: Single Cycle
Cycle time long enough for longest instruction
Shorter instructions waste time
No overlap
Clk
Load
Store
Waste
Cycle 1
Cycle 2
Figure: Dave Patterson
Notes: Here are the timing diagrams showing the differences between the single cycle, multiple cycle, and pipeline implementations.
For example, in the pipeline implementation, we can finish executing the Load, Store, and R-type instruction sequence in seven cycles.
In the multiple clock cycle implementation, however, we cannot start executing the store until Cycle 6 because we must wait for the load instruction to complete.
Similarly, we cannot start the execution of the R-type instruction until the store instruction has completed its execution in Cycle 9.
In the Single Cycle implementation, the cycle time is set to accommodate the longest instruction, the Load instruction.
Consequently, the cycle time for the Single Cycle implementation can be five times longer than the multiple cycle implementation.
But may be more importantly, since the cycle time has to be long enough for the load instruction, it is too long for the store instruction so the last part of the cycle here is wasted.
+2 = 77 min. (X:57)

## Slide 6: MIPS Instruction Set
op
target address
0
26
31
6 bits
26 bits
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
RISC architecture:
  ALU operations only on registers
  Memory is affected only by load and store
  Instructions follow very few formats and typically are of the same size

## Slide 7: Single Cycle Execution
Need a register for PC
Add 4 each cycle to get next PC

## Slide 8: Single Cycle Execution
Fetch instruction at current PC

## Slide 9: Single Cycle Execution
Fetch 2 registers, do ALU op, write
Fetch at beginning of cycle, write at end

## Slide 10: Single Cycle Execution
Use bits from instruction in place of Reg2
Decode sets MUX to select ALU input

## Slide 11: Single Cycle Execution
Use Reg1+Imm as data address
New MUX to select data to write

## Slide 12: Single Cycle Execution
Store Reg2, ignored by ALU MUX

## Slide 13: Single Cycle Execution
NextPC as option for 1st ALU input
Choose ALU output as source for PC

## Slide 14: Single Cycle Execution
Another choice for PC from J-type target address

## Slide 15: Single Cycle Execution
Yet another choice for PC from Reg1

## Slide 16: Single Cycle Execution
MIPS Jump-and-link = function call
J-type, with return address saved in R31

## Slide 17: Single Cycle Execution
Longest path = IF + decode + register fetch + ALU + data fetch + register store

## Slide 18: Multi-Cycle Execution

## Slide 19: Multiple Cycle
Figure: Dave Patterson
Cycle time long enough for longest stage
Shorter stages waste time
Shorter instructions can take fewer cycles
No overlap
Cycle 1
Ifetch
Reg
Exec
Mem
Wr
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
Ifetch
Reg
Exec
Mem
Load
Store
Ifetch
R-type
Clk
Notes: Here are the timing diagrams showing the differences between the single cycle, multiple cycle, and pipeline implementations.
For example, in the pipeline implementation, we can finish executing the Load, Store, and R-type instruction sequence in seven cycles.
In the multiple clock cycle implementation, however, we cannot start executing the store until Cycle 6 because we must wait for the load instruction to complete.
Similarly, we cannot start the execution of the R-type instruction until the store instruction has completed its execution in Cycle 9.
In the Single Cycle implementation, the cycle time is set to accommodate the longest instruction, the Load instruction.
Consequently, the cycle time for the Single Cycle implementation can be five times longer than the multiple cycle implementation.
But may be more importantly, since the cycle time has to be long enough for the load instruction, it is too long for the store instruction so the last part of the cycle here is wasted.
+2 = 77 min. (X:57)

## Slide 20: Multi-Cycle Implementation of MIPS
Instruction fetch cycle (IF)
IR  Mem[PC]; NPC  PC + 4
Instruction decode/register fetch cycle (ID)
A  Regs[IR6..10]; B  Regs[IR11..15]; Imm  ((IR16)16 ##IR16..31)
Execution/effective address cycle (EX)
Memory ref: ALUOutput  A + Imm;
  Reg-Reg ALU: ALUOutput  A func B;
  Reg-Imm ALU: ALUOutput  A op Imm;
  Branch: ALUOutput  NPC + Imm; Cond  (A op 0)
Memory access/branch completion cycle (DM)
  Memory ref: LMD  Mem[ALUOutput] or Mem(ALUOutput]  B;
  Branch: if (cond) PC ALUOutput;
Write-back cycle (WB)
  Reg-Reg ALU: Regs[IR16..20]  ALUOutput;
  Reg-Imm ALU: Regs[IR11..15]  ALUOutput;
  Load: Regs[IR11..15]  LMD;

## Slide 21: Stages of Instruction Execution
The load instruction is the longest
All instructions follows at most the following five steps:
  Ifetch: Instruction Fetch
    Fetch the instruction from the Instruction Memory and update PC
  Reg/Dec: Registers Fetch and Instruction Decode
  Exec: Calculate the memory address
  Mem: Read the data from the Data Memory
  WB: Write the data back to the register file
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Ifetch
Reg/Dec
Exec
Mem
WB
Load
Slide: Dave Patterson
Notes: As shown here, each of these five steps will take one clock cycle to complete.
And in pipeline terminology, each step is referred to as one stage of the pipeline.
+1 = 8 min. (X:48)

## Slide 22: Pipeline
Figure: Dave Patterson
Cycle time long enough for longest stage
Shorter stages waste time
No additional benefit from shorter instructions
Overlap instruction execution
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
Clk
Load
Ifetch
Reg
Exec
Mem
Wr
Ifetch
Reg
Exec
Mem
Wr
Store
Ifetch
Reg
Exec
Mem
Wr
R-type
Notes: Here are the timing diagrams showing the differences between the single cycle, multiple cycle, and pipeline implementations.
For example, in the pipeline implementation, we can finish executing the Load, Store, and R-type instruction sequence in seven cycles.
In the multiple clock cycle implementation, however, we cannot start executing the store until Cycle 6 because we must wait for the load instruction to complete.
Similarly, we cannot start the execution of the R-type instruction until the store instruction has completed its execution in Cycle 9.
In the Single Cycle implementation, the cycle time is set to accommodate the longest instruction, the Load instruction.
Consequently, the cycle time for the Single Cycle implementation can be five times longer than the multiple cycle implementation.
But may be more importantly, since the cycle time has to be long enough for the load instruction, it is too long for the store instruction so the last part of the cycle here is wasted.
+2 = 77 min. (X:57)

## Slide 23: Multi-Cycle Execution

## Slide 24: Pipeline

## Slide 25: Pipeline Datapath
Data Stationary
Every stage must be completed in one clock cycle to avoid stalls
Values must be latched to ensure correct execution of instructions
The PC multiplexer spans stages, more on that later.

## Slide 26: Instruction Pipelining
IFetch
Dec
Exec
Mem
WB
IFetch
Dec
Exec
Mem
WB
IFetch
Dec
Exec
Mem
WB
IFetch
Dec
Exec
Mem
WB
IFetch
Dec
Exec
Mem
WB
IFetch
Dec
Exec
Mem
WB
Program Flow
Time
Pipelining improves performance by increasing instruction throughput
Start handling next instruction while the current instruction is in progress
Feasible when different devices at different stages

## Slide 27: Example of Instruction Pipelining
Ideal and upper bound for speedup is number of stages in the pipeline
Time between first & fourth instructions is 3  2 = 6 ns
Time between first & fourth instructions is 3  8 = 24 ns

## Slide 28: Pipeline Performance
Pipeline increases the instruction throughput
  not execution time of an individual instruction
An individual instruction can be slower:
  Additional pipeline control
  Imbalance among pipeline stages
Suppose we execute 100 instructions:
  Single Cycle Machine
    45 ns/cycle x 1 CPI x 100 inst = 4500 ns
  Multi-cycle Machine
    10 ns/cycle x 4.2 CPI (due to inst mix) x 100 inst = 4200 ns
  Ideal 5 stages pipelined machine
    10 ns/cycle x (1 CPI x 100 inst + 4 cycle drain) = 1040 ns
Lose performance due to fill and drain

## Slide 29: Pipeline Stage Interface

## Slide 30: Pipeline Hazards
Cases that affect instruction execution semantics and thus need to be detected and corrected
Hazards types
  Structural hazard: attempt to use a resource two different ways at same time
    Single memory for instruction and data
  Data hazard: attempt to use item before it is ready
    Instruction depends on result of prior instruction still in the pipeline
  Control hazard: attempt to make a decision before condition is evaluated
    branch instructions
Hazards can always be resolved by waiting

## Slide 31: Visualizing Pipelining
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Slide: David Culler

## Slide 32: Example: One Memory Port/Structural Hazard
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Instr 3
Instr 4
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
DMem
Structural Hazard
Slide: David Culler

## Slide 33: Resolving Structural Hazards
Wait
  Must detect the hazard
    Easier with uniform ISA
  Must have mechanism to stall
    Easier with uniform pipeline organization
Throw more hardware at the problem
  Use instruction & data cache rather than direct access to memory

## Slide 34: Detecting and Resolving Structural Hazard
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Stall
Instr 3
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg
Bubble
Bubble
Bubble
Bubble
Bubble
Slide: David Culler

## Slide 35: Stalls & Pipeline Performance
Assuming all stages are balanced

## Slide 36: Data Hazards
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Time (clock cycles)
IF
ID/RF
EX
MEM
WB
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Slide: David Culler
Reg
ALU
DMem
Ifetch
Reg

## Slide 37: Three Generic Data Hazards
Read After Write (RAW) InstrJ tries to read operand before InstrI writes it
Caused by a “Data Dependence” (in compiler nomenclature). This hazard results from an actual need for communication.
Slide: David Culler
I: add r1,r2,r3
J: sub r4,r1,r3

## Slide 38: Three Generic Data Hazards
Write After Read (WAR) InstrJ writes operand before InstrI reads it
Called an “anti-dependence” in compilers.
  This results from reuse of the name “r1”.
Can’t happen in 5-stage MIPS
Can happen in out-of-order execution pipelines:
  sub is waiting for multiply, but add is not
  Could start add early
  But the add might finish before the sub reads r1
  sub will get the wrong r1 data.
I: mul r3,r1,r7
J: sub r4,r1,r3
K: add r1,r2,r5
Slide: David Culler

## Slide 39: Three Generic Data Hazards
Write After Write (WAW) InstrJ writes operand before InstrI writes it.
Called an “output dependence” in compilers
  This also results from the reuse of name “r1”.
Can’t happen in 5-stage MIPS
Can happen in out-of-order execution pipelines
  Start both add and mul together
  add finishes first, writes r1
  mul finishes second, overwrites r1!
I: mul r1,r4,r3
J: add r1,r2,r3
K: sub r6,r1,r7
Slide: David Culler

## Slide 40: Data Hazards
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Time (clock cycles)
IF
ID/RF
EX
MEM
WB
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Slide: David Culler
Reg
ALU
DMem
Ifetch
Reg

## Slide 41: Forwarding to Avoid Data Hazard
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Slide: David Culler

## Slide 42: HW Change for Forwarding
MEM/WR
ID/EX
EX/MEM
Data
Memory
ALU
mux
mux
Registers
NextPC
Immediate
mux
Slide: David Culler

## Slide 43: Data Hazard Even with Forwarding
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
or r8,r1,r9
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Slide: David Culler
Notes: MIPS actutally didn’t interlecok: MPU without Interlocked Pipelined Stages

## Slide 44: Resolving Load Hazards
Adding hardware? How? Where?
Detection?
Compilation techniques?
What is the cost of load delays?
Slide: David Culler

## Slide 45: Resolving the Load Data Hazard
Time (clock cycles)
or r8,r1,r9
I
n
s
t
r.
O
r
d
e
r
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
Reg
ALU
DMem
Ifetch
Reg
Ifetch
ALU
DMem
Bubble
Reg
Reg
Ifetch
ALU
DMem
Reg
Bubble
Ifetch
ALU
DMem
Reg
Bubble
Reg
How is this different from the instruction issue stall?
Slide: David Culler

## Slide 46: Software Scheduling to Avoid Load Hazards
Try producing fast code for
a = b + c;
d = e – f;
assuming a, b, c, d ,e, and f in memory.
Slow code:
LW Rb,b
LW Rc,c
ADD Ra,Rb,Rc
SW a,Ra
LW Re,e
LW Rf,f
SUB Rd,Re,Rf
SW d,Rd
Fast code:
LW Rb,b
LW Rc,c
LW Re,e
ADD Ra,Rb,Rc
LW Rf,f
SW a,Ra
SUB Rd,Re,Rf
SW d,Rd
Slide: David Culler

## Slide 47: Instruction Set Connection
What is exposed about this organizational hazard in the instruction set?
k cycle delay?
  bad, CPI is not part of ISA
k instruction slot delay
  load should not be followed by use of the value in the next k instructions
Nothing, but code can reduce run-time delays
Slide: David Culler

## Slide 48: Pipeline Hazards
Cases that affect instruction execution semantics and thus need to be detected and corrected
Hazards types
  Structural hazard: attempt to use a resource two different ways at same time
    Single memory for instruction and data
  Data hazard: attempt to use item before it is ready
    Instruction depends on result of prior instruction still in the pipeline
  Control hazard: attempt to make a decision before condition is evaluated
    branch instructions
Hazards can always be resolved by waiting

## Slide 49: Control Hazard on Branches Three Stage Stall
10: beq r1,r3,36
14: and r2,r3,r5
18: or r6,r1,r7
22: add r8,r1,r9
36: xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Slide: David Culler

## Slide 50: Datapath Reminder

## Slide 51: Example: Branch Stall Impact
If 20% branch, 3-cycle stall significant!
Two part solution:
  Determine branch taken or not sooner, AND
  Compute taken branch address earlier
MIPS branch tests if register = 0 or  0
MIPS Solution:
  Move Zero test to ID/RF stage
  Adder to calculate new PC in ID/RF stage
  1 clock cycle penalty for branch versus 3
Slide: David Culler

## Slide 52: Pipelined MIPS Datapath
Add
Zero?
Figure: Dave Patterson

## Slide 53: Four Branch Hazard Alternatives
Stall until branch direction is clear
Predict Branch Not Taken
  Execute successor instructions in sequence
  “Squash” instructions in pipeline if branch taken
  Advantage of late pipeline state update
  47% MIPS branches not taken on average
  PC+4 already calculated, so use it to get next instruction
Predict Branch Taken
  53% MIPS branches taken on average
  But haven’t calculated branch target address in MIPS
    MIPS still incurs 1 cycle branch penalty
    Other machines: branch target known before outcome
Slide: David Culler

## Slide 54: Four Branch Hazard Alternatives
Delayed Branch
  Always execute instructions immediately after the branch instruction, then branch branch instruction always execute1 ........ always executen not taken1
  not taken2
  ........
  branch target if taken
  1 slot delay allows proper decision and branch target address in 5 stage pipeline
  MIPS used this
Branch delay of length n
Slide: David Culler

## Slide 55: Branch-Delay Scheduling Requirements
Limitation on delayed-branch scheduling arise from:
  Restrictions on instructions scheduled into the delay slots
  Ability to predict at compile-time whether a branch is likely to be taken
May have to fill with a no-op instruction
  Average 30% wasted
Additional PC is needed to allow safe operation in case of interrupts (more on this later)

## Slide 56: Example: Evaluating Branch Alternatives
Assume:
14% Conditional & Unconditional
65% Taken; 52% Delay slots not usefully filled
Scheduling Scheme | Branch Penalty | CPI | Pipeline Speedup | Speedup vs stall
Stall pipeline | 3.00 | 1.42 | 3.52 | 1.00
Predict taken | 1.00 | 1.14 | 4.39 | 1.25
Predict not taken | 1.00 | 1.09 | 4.58 | 1.30
Delayed branch | 0.52 | 1.07 | 4.66 | 1.32
Slide: David Culler
Notes: Stall: 1+.14(branches)*3(cycle stall)
Taken: 1+.14(branches)*(.65(taken)*1(delay to find address)+.35(not taken)*1(penalty))
Not taken: 1+.14*(.65(taken)*1+[.35(not taken)*0])
Delayed: 1+.14*(.52(not usefully filled)*1)

## Slide 57: Recall Branch Penalties