## Slide 1: Some Intel CPU examples
Figures and data from Arstechnica
arstechnica.com/old/content/2004/07/pentium-1.ars
arstechnica.com/old/content/2001/05/p4andg4e.ars
arstechnica.com/old/content/2004/02/pentium-m.ars
arstechnica.com/hardware/news/2006/04/core.ars
arstechnica.com/hardware/news/2008/04/what-you-need-to-know-about-nehalem.ars

## Slide 2: Pentium
Dual Issue
Two 5-stage integer pipes (some restrictions)
  1: Prefetch/fetch
  2: Decode 1
    Branch predict (75%)
  3: Decode 2
    Address computation
  4: Execute
  5: Write back
6-stage float pipe

## Slide 3: Pentium Pro, II, III
3 instruction issue
  2 simple, 1 complex
40-entry ROB
  Rotating queue
Execution
  5 issue ports
  Store addr/data
  1 cycle EX for most
  *÷ 4-cycle latency, 1 cycle issue

## Slide 4: Pentium Pro, II, III
12-stage pipe
  1-4.5: BTB & IF
    Prediction 90+%
  4.5-6: Decode
  7: ROB rename
  8: Write RS (20 inst.)
  9: Issue
  10: Execute
  11-12: Retire

## Slide 5: P4 (Pentium 4)
Trace cache
  Internal RISC ISA
  90% Hit rate
  ROM for long instructions
  Mini BTB for trace cache branches
20+ stage pipeline
  More on trace cache miss

## Slide 6: P4 (Pentium 4)
1-2: Trace cache next IP
3-4: Trace cache fetch
5: Drive signals
6-8: Allocate & Rename
  128 µreg
9: Queue
10-12: Schedule
13-14: Dispatch
  Up to 6 per cycle
15-16: Register file
17: Execute
18: Flags
19: Branch check
20: Drive signals

## Slide 7: Pentium M
Branch prediction
  4k BTB
  Loop predictor
  Indirect predictor
µop fusion
  Avoid ROB

## Slide 8: Core
← 96 entry

## Slide 9: Core Decode
4-7 issue to 7 µop
  Multiple x86 to one µop
  Macro-fusion merges across x86 ops
  µop fusion to avoid ROB

## Slide 10: Memory Speculation
store A, addr1
-stall-
load addr2, B
-stall-
add B,C,D
If addr1 = addr2
Aliasing
load addr2, B
store A, add1
add B,C,D
If addr1 ≠ addr2
Assume no aliasing
Restart if wrong

## Slide 11: Nehalem
Rely on hyperthreading
128-entry ROB
36-entry RS