## Slide 1: CMSC 611: Advanced Computer Architecture
Cache
Part II
Some material adapted from Mohamed Younis, UMBC CMSC 611 Spr 2003 course slides
Some material adapted from Hennessy & Patterson / © 2003 Elsevier Science

## Slide 2: Measuring Cache Performance
Compute Average Access Time
Miss penalty for L1 is the average access time for L2
Together, computes Average Memory Access Time (AMAT)

## Slide 3: Determining Block Size
Miss
Penalty
Block Size
Miss
Rate
Exploits Spatial Locality
Fewer blocks:
compromises
temporal locality
Average
Access
Time
Increased Miss Penalty
& Miss Rate
Block Size
Block Size
Larger block size take advantage of spatial locality BUT:
  Larger block size means larger miss penalty:
    Takes longer time to fill up the block
  If block size is too big relative to cache size, miss rate will go up
    Too few cache blocks
Typical size today = 64 bytes (16 32-bit words)
Average Access Time = Hit Time + Miss Penalty * Miss Rate

## Slide 4: Block Placement
Cache utilization
Hardware Complexity
Set number = (Block number) modulo (Number of sets in the cache)
Increased flexibility of block placement reduces probability of cache misses

## Slide 5: Direct-Mapped Cache
Cache block address = (Block address) modulo (Number of cache blocks)
Memory words can be mapped only to one cache block
Cache Data
Valid Bit
Byte 0
Byte 1
Byte 3
Cache Tag
Byte 2
Worst case is to keep replacing a block followed by a miss for it: Ping Pong Effect
To reduces misses:
  make the cache size bigger

## Slide 6: Cache Size
Size depends on:
  # cache blocks
  Tag size
  Block size
Example:
  For 32-bit address 1024 4-byte blocks
  Data size = 4*1024 B = 4096 B
  Physical size = (data+tag+valid)*lines = (32+20+1)*1024 bits = 53*1024 bits = 6784 B

## Slide 7: Cache with Multi-Word/Block
Takes advantage of spatial locality to improve performance
Cache block address = (Block address) mod (Number of cache blocks)
Block address = (byte address) / (bytes per block)

## Slide 8: Locating a Block in Associative Cache
Tag size increases with higher level of associativity

## Slide 9: Fully Associative Cache
:
Cache Data
Byte 0
0
4
31
:
Cache Tag (27 bits long)
Valid Bit
:
Byte 1
Byte 31
:
Byte 32
Byte 33
Byte 63
:
Cache Tag
Byte Select
Ex: 0x01
X
X
X
X
X
Forget about the Cache Index
Compare the Cache Tags of all cache entries in parallel
Example: Block Size = 32 Byte blocks, we need N 27-bit comparators
By definition: Conflict Miss = 0 for a fully associative cache
Notes: Direct mapped = simple / fully associative = complex
Like N-way set associative with N = # cache entries
i.e. no cache index bits in address.
Very hardware intensive: usually, fully associative cache is limited to 64 or less entries.
Never conflict, but can have Capacity Miss (on 65th item in 64-element cache)

## Slide 10: Handling Cache Misses
Read misses bring blocks from memory
Write access requires careful maintenance of consistency between cache and main memory
Two write strategies:
  Write through: write to both cache and memory
    Read misses cannot result in writes
    No allocation of a cache block is needed
    Always combined with write buffers so that don’t wait for slow memory
  Write back: write cache only; write to memory when cache block is replaced
    Is block clean or dirty?
    No writes to slow memory for repeated write accesses
    Requires allocation of a cache block

## Slide 11: Write Through via Buffering
Processor
Cache
Write Buffer
DRAM
Processor writes data into the cache and the write buffer
Memory controller writes contents of the buffer to memory
Increased write frequency can cause saturation of write buffer
If CPU cycle time too fast and/or too many store instructions in a row:
  Store buffer will overflow no matter how big you make it
  The CPU Cycle Time get closer to DRAM Write Cycle Time
Write buffer saturation can be handled by installing a second level (L2) cache
Processor
Cache
Write Buffer
DRAM
L2
Cache

## Slide 12: Block Replacement Strategy
Empirical results indicates less significance of replacement strategy with
increased cache sizes
Straight forward for Direct Mapped since every block has only one location
Set Associative or Fully Associative:
  Random: pick any block
  LRU (Least Recently Used)
    requires tracking block reference
    for two-way set associative cache, reference bit attached to every block
    more complex hardware is needed for higher level of cache associativity

## Slide 13: Measuring Cache Performance
For write-through scheme:
Hard to control, assume enough buffer size
To enhance cache performance, one can:
  Reduce the miss rate (e.g. diminishing blocks collisions)
  Reduce the miss penalty (e.g. adding multi-level caching)
  Enhance hit access time (e.g. simple and small cache)

## Slide 14: Example
Assume an instruction cache miss rate for gcc of 2% and a data cache miss rate of 4%. If a machine has a CPI of 1.2 without any memory stalls and the miss penalty is 40 cycles, determine how much faster a machine would run with a perfect cache that never missed. Assume 36% combined frequencies for load and store instructions
Answer:
  Assume number of instructions = I
  Instruction miss cycles = I  2%  40 = 0.8  I
  Data miss cycles = I  36%  4%  40 = 0.56  I
  Total number of memory-stall cycles = 0.8 I + 0.56 I = 1.36 I
  The CPI with memory stalls = 1.2 + 1.36 = 2.56

## Slide 15: Classifying Cache Misses
Compulsory
  First access to a block not in cache
  Also called cold start or first reference misses
  (Misses in even an Infinite Cache)
Capacity
  If the cache cannot contain all needed blocks
  Due to blocks discarded and re-retrieved
  (Misses in Fully Associative Cache)
Conflict
  Set associative or direct mapped: too many blocks in set
  Also called collision or interference
  (Misses in N-way Associative Cache)
Notes: Intuitive Model by Mark Hill

## Slide 16: Miss Rate Distribution
Conflict
Based on SPEC92
Compulsory misses are small compared to other categories
Capacity misses diminish with increased cache size
Increasing associativity limits the placement conflicts

## Slide 17: Techniques for Reducing Misses
1. Larger Block Size
2. Higher Associativity
3. Victim Cache
4. Pseudo-Associativity
5. Hardware Prefetching (Instructions & Data)
6. Software Prefetching Data
7. Compiler & Code Optimizations

## Slide 18: Reduce Misses via Larger Block Size
Larger block sizes reduces compulsory misses (principle of spatial locality)
Conflict misses increase for larger block sizes since cache has fewer blocks

## Slide 19: Reduce Misses via Higher Associativity
2:1 Cache Rule:
Miss Rate for direct mapped cache of size N = Miss Rate 2-way
cache size N/2
Greater associativity comes at the expense of larger hit access time
Hardware complexity grows for high associativity and clock cycle increases

## Slide 20: Example
Assume hit time is 1 clock cycle and average miss penalty is 50 clock cycles for a direct mapped cache. The clock cycle increases by a factor of 1.10 for 2-way, 1.12 for 4-way, 1.14 for 8-way associative cache. Compare the average memory access based on the previous figure miss rates
High associativity becomes a negative aspect
A good size of direct mapped cache can be very efficient given its simplicity

## Slide 21: Victim Cache
Combines fast hit time of direct mapped yet still avoids conflict misses
  Adds small fully associative cache between the direct mapped cache and memory to place data discarded from cache
  Jouppi [1990]: 4-entry victim cache removed 20% to 95% of conflicts for a 4 KB direct mapped data cache
  Used in HP and Alpha

## Slide 22: Pseudo-Associativity Mechanism
Combine fast hit time of Direct Mapped and lower conflict misses of 2-way set associative
Divide cache: on a miss, check other half of cache to see if there, if so have a pseudo-hit
To limit the impact of hit time variability on performance, swap block contents
Drawback: CPU pipeline is hard if hit takes 1 or 2 cycles
  Better for caches not tied directly to processor (L2)
  Used in MIPS R1000 L2 cache, similar in UltraSPARC

## Slide 23: H/W Pre-fetching of Instructions & Data
Hardware pre-fetches instructions and data while handing other cache misses
  Assume pre-fetched items will be referenced shortly
Pre-fetching relies on having extra memory bandwidth that can be used without penalty
Examples of Instruction Pre-fetching:
  Alpha 21064 fetches 2 blocks on a miss
  Extra block placed in “stream buffer”
  On miss check stream buffer
Works with data blocks too:
  Jouppi [1990] 1 data stream buffer got 25% misses from 4KB cache; 4 streams got 43%
  Palacharla & Kessler [1994] for scientific programs for 8 streams got 50% to 70% of misses from 2 64KB, 4-way set associative caches

## Slide 24: Software Pre-fetching Data
for (i = 0; i < 3; i = i+1)
for (j = 0; j < 100; j = j+1)
a[i][j] = b[j][0] * b[j+1][0];
for (j = 0; j < 100; j = j+1)
pre-fetch (b[i+7][0]);
a[0][j] = b[j][0] * b[j+1][0];
for (i = 1; i < 3; i = i+1)
pre-fetch (a[i][j+7]);
a[i-1][j] = b[j][0] * b[j+1][0];
Uses special instructions to pre-fetch data:
  Load data into register (HP PA-RISC loads)
  Cache Pre-fetch: load into cache (MIPS IV, PowerPC, SPARC v. 9)
Special pre-fetching instructions cannot cause faults (undesired exceptions) since it is a form of speculative execution
Makes sense if the processor can proceed without blocking for a cache access (lock-free cache)
Loops are typical target for pre-fetching after unrolling (miss penalty is small) or after applying software pipelining (miss penalty is large)
Issuing Pre-fetch Instructions takes time
  Is cost of pre-fetch issues < savings in reduced misses?
  Higher superscalar reduces difficulty of issue bandwidth

## Slide 25: Compiler and Code-based Cache Optimizations
Complier-based cache optimization reduces the miss rate without any hardware change
McFarling [1989] reduced caches misses by 75% (8KB direct mapped / 4 byte blocks)
For Instructions
  Reorder procedures in memory to reduce conflict
  Profiling to determine likely conflicts among groups of instructions
For Data
  Splitting Arrays: remove unneeded elements from cache fetch
  Merging Arrays: improve spatial locality by single array of compound elements vs. two arrays
  Loop Interchange: change nesting of loops to access data in order stored in memory
  Loop Fusion: Combine two independent loops that have same looping and some variables overlap
  Blocking: Improve temporal locality by accessing “blocks” of data repeatedly vs. going down whole columns or rows

## Slide 26: Array Splitting
Struct or class includes extra data
Reduces locality
Array of Structures (AoS)
struct Particle {
float x;
float y;
float z;
int state;
float startTime;
};
Particle data[NUM];
Structure of Arrays (SoA)
struct Particles {
float x[NUM];
float y[NUM];
float z[NUM]
int state[NUM];
float startTime[NUM];
};
Particles data
Used together
Seldom used

## Slide 27: Array Merging
Structure of arrays of structures (SoAoS)
Fetch elements used together at once
SoAoS
struct Particles {
vector position[NUM];
int state[NUM];
float startTime[NUM];
};
Particles data
SoA
struct Particles {
float x[NUM];
float y[NUM];
float z[NUM];
int state[NUM];
float startTime[NUM];
};
Particles data

## Slide 28: Loop Interchange
Before
for (j=0; j<100; ++j)
for (i=0; i<5000; ++i)
x[i][j] = k * x[i][j];
After
for (i=0; i<5000; ++i)
for (j=0; j<100; ++j)
x[i][j] = 2 * x[i][j];
Sequential accesses instead of striding through memory every 100 words; improved spatial locality
Consider array layout in memory
…
x[0][0]
x[0][1]
x[0][99]
x[1][0]
x[1][1]
x[1][99]
…
⋮
⋮
⋮
x[0][ 0]
x[0][ 1]
Logical Layout
Physical Layout
⋮
x[0][99]
x[1][ 0]

## Slide 29: Loop Fusion
Accessing array “a” and “c” would have caused twice the number of misses without loop fusion
Combine loops to avoid capacity misses
Before
for(i=0; i<N; ++i)
for(j=0; j<N; ++j)
a[i][j] = c[i][j]/b[i][j]
for(i=0; i<N; ++i)
for(j=0; j<N; ++j)
d[i][j] = a[i][j] + c[i][j];
After
for(i=0; i<N; ++i)
for(j=0; j<N; ++j) {
a[i][j] = c[i][j]/b[i][j]
d[i][j] = a[i][j] + c[i][j];
}

## Slide 30: Blocking
Matrix Multiply
for (i = 0; i < N; ++i)
for (j = 0; j < N; ++j) {
r = 0;
for (k = 0; k < N; ++k)
r = r + y[i][k] * z[k][j];
x[i][j] = r;
}
}
Two Inner Loops:
  Read all NxN elements of z[]
  Read N elements of 1 row of y[] repeatedly
  Write N elements of 1 row of x[]
Capacity Misses funct of N & Cache Size:
  3  N  N  4 bytes = no capacity misses;
Compute on B  B sub-matrix that fits

## Slide 31: Blocking
B called Blocking Factor
Memory words accessed
2N3 + N2  2N3/B +N2
Conflict misses can go down too
Blocking is also useful for register allocation
Block Multiply
for (jj=0; jj<N; jj = jj+B) {
for (kk=0; kk<N; kk = kk+B) {
for (i=0; i<N; ++i) {
for (j=jj; j<min(jj+B-1,N); ++j) {
r = 0;
for (k=kk; k<min(kk+B-1,N); ++k)
r = r + y[i][k] * z[k][j];
x[i][j] = x[i][j] + r;
}}}}

## Slide 32: Blocking Factor
Traditionally blocking is used to reduce capacity misses relying on high associativity to tackle conflict misses
Choosing smaller blocking factor than the cache capacity can also reduce conflict misses (fewer words are active in cache)
Lam et al [1991] a blocking factor of 24 had a fifth the misses compared to a factor of 48 despite both fit in cache

## Slide 33: Cache Oblivious Orders
Nest blocks of different sizes
Ensures against different cache sizes
More addressing computation

## Slide 34: Efficiency of Code-Based Cache Opt.

## Slide 35: Reducing Miss Penalty
Read Priority over Write
Sub-block Placement
Merging Write Buffer
Victim Cache
Early Restart and Critical Word First
Non-blocking Caches
  Hit under Miss
  Miss under Miss
Extra Cache Levels

## Slide 36: Read Priority over Write on Miss
Write through with write buffers offer RAW conflicts with main memory reads on cache misses
If simply wait for write buffer to empty, might increase read miss penalty (old MIPS 1000 by 50% )
Check write buffer contents before read; if no conflicts, let the memory access continue
Processor
Cache
Write Buffer
DRAM
Write Back?
  Read miss replacing dirty block
  Normal: Write dirty block to memory, and then do the read
  Instead copy the dirty block to a write buffer, then do the read, and then
  do the write
  CPU stall less since restarts as soon as do read

## Slide 37: Sub-block Placement
Originally invented to reduce tag storage while avoiding the increased miss penalty caused by large block sizes
Enlarge the block size while dividing each block into smaller units (sub-blocks) and thus does not have to load full block on a miss
Include valid bits per sub-block to indicate the status of the sub-block (in cache or not)
Valid Bits

## Slide 38: Early Restart and Critical Word First
block
Don’t wait for full block to be loaded before restarting CPU
  Early restart
    As soon as the requested word of the block arrives, send it to the CPU and let the CPU continue execution
  Critical Word First
    Request the missed word first from memory
    Also called wrapped fetch and requested word first
Complicates cache controller design
CWF generally useful only in large blocks
Given spatial locality programs tend to want next sequential word, limits benefit

## Slide 39: Victim Cache
Lower both miss rate
Reduce average miss penalty
Slightly extend the worst case miss penalty

## Slide 40: Non-blocking Caches
Early restart still waits for the requested word to arrive before the CPU can continue execution
For machines that allows out-of-order execution using a scoreboard or a Tomasulo-style control the CPU should not stall on cache misses
“Non-blocking cache” or “lock-free cache” allows data cache to continue to supply cache hits during a miss
“hit under miss” reduces the effective miss penalty by working during miss vs. ignoring CPU requests
“hit under multiple miss” or “miss under miss” may further lower the effective miss penalty by overlapping multiple misses
  Significantly increases the complexity of the cache controller as there can be multiple outstanding memory accesses
  Requires multiple memory banks (otherwise cannot support)
  Pentium Pro allows 4 outstanding memory misses

## Slide 41: Performance of Non-blocking Caches
Benchmark
Ratio of the average memory stall time

## Slide 42: Second Level Cache
The previous techniques reduce the impact of the miss penalty on the CPU
  L2 cache handles the cache-memory interface
Measuring cache performance
Local miss rate
  misses in this cache divided by the total number of memory accesses to this cache (MissRateL2)
Global miss rate (& biggest penalty!)
  misses in this cache divided by the total number of memory accesses generated by the CPU (MissRateL1  MissRateL2)

## Slide 43: Local vs Global Misses
(Global miss rate close to single level cache rate provided L2 >> L1)

## Slide 44: L2 Cache Parameters
Block size of second-level cache (byte)
Relative execution time
32 bit bus
512KB cache
L1 cache directly affects the processor design and clock cycle: should be simple and small
Bulk of optimization techniques can go easily to L2 cache
Miss-rate reduction more practical for L2
Considering the L2 cache can improve the L1 cache design,
  e.g. use write-through if L2 cache applies write-back

## Slide 45: Reducing Hit Time
Average Access Time = Hit Time x (1 - Miss Rate) + Miss Time x Miss Rate
Hit rate is typically very high compared to miss rate
  any reduction in hit time is magnified
Hit time critical: affects processor clock rate
Three techniques to reduce hit time:
  Simple and small caches
  Avoid address translation during cache indexing
  Pipelining writes for fast write hits
Simple and small caches
Design simplicity limits control logic complexity and allows shorter clock cycles
On-chip integration decreases signal propagation delay, thus reducing hit time
  Alpha 21164 has 8KB Instruction and 8KB data cache and 96KB second level cache to reduce clock rate