## Slide 1: CMSC 611: Advanced Computer Architecture
Distributed Shared Memory
Most slides adapted from David Patterson. Some from Mohomed Younis

## Slide 2: Centralized Shared Memory
Processors share a single centralized memory
Feasible for small processor count to limit memory contention
Model for multi-core CPUs
Processor
Processor
Processor
Processor
One or more levels of cache
One or more levels of cache
One or more levels of cache
One or more levels of cache
Zero or more levels of cache
Memory
I/O

## Slide 3: Distributed Memory
Uses physically distributed memory to support large processor counts (to avoid memory contention)
Advantages
  Allows cost-effective way to scale the memory bandwidth
  Reduces memory latency
Disadvantage
  Increased complexity of communicating data
Proc
Cache
Mem
Proc
Cache
Mem
Proc
Cache
Mem
Proc
Cache
Mem
Proc
Cache
Mem
Proc
Cache
Mem
Proc
Cache
Mem
Proc
Cache
Mem

## Slide 4: NUMA vs. UMA
PE = Processing Element
UMA = Uniform Memory Access
  Shared memory
  Same cost for any PE to access
NUMA = Non-Uniform Memory Access
  All memory is associated with some PE
  Faster for that PE, slower for other PEs

## Slide 5: Shared Address Model
Physical locations
  Each PE can name every physical location in the machine
Shared data
  Each process can name all data it shares with other processes

## Slide 6: Shared Address Model
Data transfer
  Use load and store, VM maps to local or remote location
  Extra memory level: cache remote data
  Significant research on making the translation transparent and scalable for many nodes
    Handling data consistency and protection challenging
    Latency depends on the underlying hardware architecture (bus bandwidth, memory access time and support for address translation)
    Scalability is limited given that the communication model is so tightly coupled with process address space

## Slide 7: Three Fundamental Issues (#1: Naming)
What data is shared?
How it is addressed?
What operations can access data?
How processes refer to each other?
Choice of naming affects code produced by a compiler
  Just remember and load address or keep track of processor number and local virtual address for message passing
Choice of naming affects replication of data
  In cache memory hierarchy or via SW replication and consistency

## Slide 8: Naming Address Spaces
Global physical address space
  any processor can generate, address and access it in a single operation
Global virtual address space
  if the address space of each process can be configured to contain all shared data of the parallel program
    memory can be anywhere: virtual address translation handles it
Segmented shared address space
  locations are named <process number, address> uniformly for all processes of the parallel program

## Slide 9: Three Fundamental Issues (#2: Synchronization)
To cooperate, processes must coordinate
Message passing is implicit coordination with transmission or arrival of data
Shared address → additional operations to explicitly coordinate: e.g., write a flag, awaken a thread, interrupt a processor

## Slide 10: Three Fundamental Issues (#3: Latency & Bandwidth)
Bandwidth
  Need high bandwidth in communication
  Match limits in network, memory, and processor
  Overhead to communicate is a problem in many machines
Latency
  Affects performance, since processor may have to wait
  Affects ease of programming, since requires more thought to overlap communication and computation
Latency Hiding
  How can a mechanism help hide latency?
  Examples: overlap message send with computation, pre-fetch data, switch to other tasks

## Slide 11: Snooping Cache Coherency
Send all requests for data to all processors
Processors snoop to see if they have a copy and respond accordingly
Requires broadcast, since caching information is at processors
Works well with bus (natural broadcast medium)

## Slide 12: Directory Cache Coherency
Keep track of what is being shared in one centralized place
Distributed memory ⇒ distributed directory for scalability (avoids bottlenecks)
Send point-to-point requests to processors via network
Scales better than Snooping
Actually existed before Snooping-based schemes

## Slide 13: Distributed Directory Multiprocessors
Directory per cache that tracks state of every block in every cache
  Which caches have a block, dirty vs. clean, ...
  Info per memory block vs. per cache block?
    simpler protocol (centralized/one location)
    directory is O(memory size) vs. O(cache size)
To prevent directory from being a bottleneck
  Distribute directory entries with memory
  Each tracks of which processor has their blocks

## Slide 14: Directory Protocol
Similar to Snoopy Protocol: Three states
  Shared: Multiple processors have the block cached and the contents of the block in memory (as well as all caches) is up-to-date
  Uncached No processor has a copy of the block (not valid in any cache)
  Exclusive: Only one processor (owner) has the block cached and the contents of the block in memory is out-to-date (the block is dirty)
In addition to cache state, must track which processors have data when in the shared state
  Usually bit vector, 1 if processor has copy

## Slide 15: Directory Protocol
Keep it simple(r):
  Writes to non-exclusive data = write miss
  Processor blocks until access completes
  Assume messages received and acted upon in order sent
Terms: typically 3 processors involved
  Local node where a request originates
  Home node where the memory location of an address resides
  Remote node has a copy of a cache block, whether exclusive or shared
No bus and do not want to broadcast:
  Interconnect no longer single arbitration point
  All messages have explicit responses

## Slide 16: Example Directory Protocol
Message sent to directory causes two actions:
  Update the directory
  More messages to satisfy request
We assume operations atomic, but they are not; reality is much harder; must avoid deadlock when run out of buffers in network

## Slide 17: Directory Protocol Messages
Type | SRC | DEST | MSG
Read miss | local cache | home directory | P,A
P has read miss at A; request data and make P a read sharer |  |  | 
Write miss | local cache | home directory | P,A
P has write miss at A; request data and make P exclusive owner |  |  | 
Invalidate | home directory | remote cache | A
Invalidate shared data at A |  |  | 
Fetch | home directory | remote cache | A
Fetch block A home; change A remote state to shared |  |  | 
Fetch/invalidate | home directory | remote cache | A
Fetch block A home; invalidate remote copy |  |  | 
Data value reply | home directory | local cache | D
Return data value from home memory |  |  | 
Data write back | remote cache | home directory | A,D
Write back data value for A |  |  | 

## Slide 18: Cache Controller State Machine
State machine for CPU requests for each memory block
States identical to snoopy case
  Transactions very similar.
    Miss messages to home directory
    Explicit invalidate & data fetch requests

## Slide 19: Directory Controller State Machine
State machine
for Directory requests for each
memory block
Same states and structure as the transition diagram for an individual cache
  Actions:
    update of directory state
    send messages to satisfy requests
  Tracks all copies of each memory block
    Sharers set implementation can use a bit vector of a size of # processors for each block

## Slide 20: Example
P2: Write 20 to A1
Assumes memory blocks A1 and A2 map to same cache block

## Slide 21: Example
P2: Write 20 to A1
WrMs
P1
A1
A1
Ex
{P1}
Excl.
A1
10
DaRp
P1
A1
0
Assumes memory blocks A1 and A2 map to same cache block

## Slide 22: Example
P2: Write 20 to A1
WrMs
P1
A1
A1
Ex
{P1}
Excl.
A1
10
DaRp
P1
A1
0
Excl.
A1
10
Assumes memory blocks A1 and A2 map to same cache block

## Slide 23: Example
P2: Write 20 to A1
WrMs
P1
A1
A1
Ex
{P1}
Excl.
A1
10
DaRp
P1
A1
0
Excl.
A1
10
Shar.
A1
RdMs
P2
A1
Shar.
A1
10
Ftch
P1
A1
10
10
Shar.
A1
10
DaRp
P2
A1
10
A1
Shar.
{P1,P2}
10
A1
Write Back
Assumes memory blocks A1 and A2 map to same cache block

## Slide 24: Example
P2: Write 20 to A1
Excl.
A1
10
DaRp
P1
A1
0
Excl.
A1
10
Shar.
A1
RdMs
P2
A1
Shar.
A1
10
Ftch
P1
A1
10
10
Shar.
A1
10
DaRp
P2
A1
10
A1
Shar.
{P1,P2}
10
A1
Excl.
A1
20
WrMs
P2
A1
10
Inv.
Inval.
P1
A1
A1
Excl.
{P2}
10
Assumes memory blocks A1 and A2 map to same cache block

## Slide 25: Example
P2: Write 20 to A1
WrMs
P1
A1
A1
Ex
{P1}
Excl.
A1
10
DaRp
P1
A1
0
Excl.
A1
10
Shar.
A1
RdMs
P2
A1
Shar.
A1
10
Ftch
P1
A1
10
10
Shar.
A1
10
DaRp
P2
A1
10
A1
Shar.
{P1,P2}
10
A1
Excl.
A1
20
WrMs
P2
A1
10
Inv.
Inval.
P1
A1
A1
Excl.
{P2}
10
WrBk
P2
A1
20
A1
Unca.
{}
20
Excl.
A2
40
DaRp
P2
A2
0
A2
Excl.
{P2}
0
WrMs
P2
A2
A2
Excl.
{P2}
0
Assumes memory blocks A1 and A2 map to same cache block